## Slide 1
Work Plan
WP9 Sustainable Development Strategy
Working document
N. Arnaud, S.Katsanevas, M.Marsella
1. Carbon footprint (including computing and transportation)
2. Liaison with Climate Change and Geoscience
3. Landscape and Environmental impact
2 meetings up to now:
EGO for power issues
Maria, Nicolas Stavros and Chief IT of Roma1 for distribution of work

## Slide 2: WP9.1 Carbon footprint (including computing and transportation)
We start our study with a comparison with the existing footprint of the current 2nd Generation detectors., based on a study done 2 years ago.
SWP9.1.1 Power.
  Total power usage: LLO reports that they use on average 800 kW. This leads to a rough yearly number of kWh of 800*24*365 of 5,088,000 kWh -- 5GWh.
  For LHO: we average 700,000kWh per month. A good estimate for the year is 8,4 GWh. A very nice fact: the power for LHO is mostly renewables.
  Virgo:average power consumption of the EGO site is 320 kW annual energy consumption of the EGO site is between 2.4 to 3.2 GWh/year. In 2019 it has been 2.7 GWh.
  KAGRA: Power (kWh) consumption at KAGRA site.2,2 MWh.
  LHO is >50% higher power usage than LLO. Surprising?  Weather
  Summary power usage: LHO: 8.4 GWh (100% renewables!), LLO: 5 GWh, Virgo: 2.7 GWh, KAGRA: 2.2 GWh Total is 18.3 GWh. subtracting LHO (green!), end up with 10 GWh.
  Using 1 kg CO2/kWH, get total power carbon footprint: 1e7 kg of CO2. ~1000 tons of CO2

## Slide 3: WP9.1 Carbon footprint (including computing and transportation)
  WP9.1.2 Computing. LIGO: O3 computing cycles, 500 million CPU core hours, over roughly 18–24 months Baseline computing estimate: 250 million CPU core hours per year. Power/computing comes from ~10 different sources. Caltech. Milwaukee. XSEDE. etc. Assume average carbon footprint for US power. Virgo (not known yet). Kagra: The total computing cycles of KAGRA’s dedicated clusters, assuming a duty cycle of 80% for each system. The total number is approximately 550k computing cycles/day (≈ 16M computing cycles/month). Combined computing is ~700M CPU core hours per year Supposing that 10 CPU core hours requires 0.52 kWh. So 700M CPU core hours requires 364 MWh each year.
  Using 1 kg CO2/kWH, get total power carbon footprint ~400 tons of CO2

## Slide 4: WP9.1 Carbon footprint (including computing and transportation)
WP9.1.3 Travel: Start with 2 main meetings? Start with LVK specific ones. ask LVK labs business office to give data on trips. At some point need to do poll. Also contact previous two LVK meetings. 3 Virgo weeks per year. Start google doc/sheet to collect information. Some scientific meetings are almost completely “our” community. Start with actual LVK collaboration activities (because we can influence). Exemples: Sonoma meeting: Asia (Japan, australia): 300, US: 200 Europe: 112, S. America (mostly Brazil): 12. .Using this calculator, it’s 1.3 tons of CO2 from CDG to SFO. Sonoma meeting generated roughly: 200 tons of CO2. Glasgow meeting: Using the participant country breakdown for the Glasgow LVC meeting in 2016: one calculates ~120 tons CO2
Kagra:They have lists of participants of KAGRA members to LVK related conferences and in principle could estimate the total number of km traveled, maybe separating planes and other means of transport. But we better have a common way of doing this. How do we want to estimate the impact of travel? 24th KAGRA face-to-face meeting (University of Tokyo., December 2019) Participants: 110 ~ 54 tons CO2, 5th The KAGRA International Workshop (KIW), Perugia - Italy, 2019 ~123 tons CO2; ù
Two annual international LVK conferences, plus assorted workshops: ~400 tons CO2

## Slide 5: WP9.1 Carbon footprint (including computing and transportation)
Bottom Line
Power at sites: 1000 tons CO2 per year,
Travel: 400 tons CO2 per year
Computing: 400 tons CO2 per year
The group will study the use of photovoltaic and geothermal energy.
The study will be done within the LVK collaboration
Collaboration with ET responsibles will permit the projection
Ideas to be studied
  Photovoltaic, geothermal
  Reuse dissipated energy from computing center: Le supercalculateur Jean-Zay du CNRS va alimenter le réseau de chaleur et de froid du campus urbain de Paris-Saclay. “Green Cube” at GSI, 4% de l'energie pour le refroidissement. “Virtual Data” at IJCLab (-> Michel Jouvin)
  Reuse dissipated energy from vacuum and cryogenic installations ?
  Efficient internet / wifi distribution?
  Organize passive house buildings, green car shuttle,
  Videoconferences instead of travels? how much we gain , find the numbers
  Reduce travels
Use trains/ships instead of planes/cars when possible
Methodology:: workshops, and extra measuring devices for specific consumptions.
Deliverable 1 / CO2 Impact from Power, Computing and travel.

## Slide 6: WP9.2 Liaison with Geosciene, Atmospheric science and Climate change
Earth and Astroparticle sciences share a mutual scientific culture based on common objects of study, methods and approaches. First, the Geosphere, a direct object of study of Geoscientists, is both the target and the detecting medium for Astroparticle observatories. Second, Astroparticle Physicists and Geoscientists both deal with complex natural large scale systems, deploy large sensor networks, sometimes in extreme environments (sea, desert, underground, space), use long series of precise observations acquired over long time scales, emit low latency alerts develop models relying on the state-of-the-art in fundamental physics, chemistry, biology and computer sciences.
They both can serve for measuring climate change and produce low latency alerts. The EInstein Telescope is a perfect example of the above:
Imaging (gravimetric, seismic, acoustic, muon, neutrino);
Data collection in extreme environments;
New technological means for parameter monitoring;
Contribution to the understanding and forecasting and natural alerts of natural hazards.
Eg. ET will deploy a sophisticated distributed network of sensors to evaluate and subtract environmental background: electromagnetic perturbations, non-stationary ground deformations, sea waves, cloud passage, electromagnetic waves, cosmic rays, acoustic noise vibrations, anthropogenic movements;
Exemples: Fiber or mobile sensor networks, distribution of Low Latency alerts,
Methodology: worldwide workshops
Deliverable: Studies of the use of the ET technology on measurements of the climate change, low latency alert and also quantum computing

## Slide 7: WP9.3 Landscape and Environmental impact
Site mostly underground
Surface buildings + access roads + site roads
Power grid infrastructure
Excavations: access pipes and tunnels: what to do with the excavated material?
Local food
Green transportation (on-site and to/from site):
antonella, lot de calcul par ed porter et Katsavounides/Couvares
Find the studies GWIC...
100% electrical vehicles on site
Charging stations
Transportation to/from campus: regular schedule

## Slide 8
Whom to contact:
ET ISB/VAcuum/cryo, EIB/computing, ISB/Fuentes+Maria
LVK meeting to reevaluate some of th enumbers
SKA, CTA , KM3NEt , LSST, LHC
FCC: FCC Feasibility Study (FS) 2021 -> 2025 https://indico.cern.ch/event/1055562/contributions/4460980/attachments/2286764/3886757/ECFA-FCC-2021.pdf
Platform for the the project follow-up (Roma1)
Resources asked :
2FTEx3 years 330 KE (55 KE/year) (technical side, institutional side)
Funds for workshops 50 KE
Fund for travel 20 KE