## Slide 1: A SUPER-WIDE FIELD OF VIEW CHERENKOV TELESCOPE
J. Cortina, R. López-Coto, A. Moralejo. R. Rodríguez
Pizza seminar
June 3rd, 2015

## Slide 2: IACTs are pointing instruments
Field of View (FOV) of a typical IACT (HESS ~20 deg2, CTA-SCT~50 deg2)
Fermi sky (photons in 2 years)
The whole sky = 42000 deg2
By the way, compare with “wide FOV” in optical telescopes: DECam has 4 deg2, SDSS has 7 deg2, LSST will have 10 deg2

## Slide 3: Surveys with IACTs
Say we need 10h to achieve enough sensitivity. We would need 10000 hours to scan the whole sky: telescopes need ~10 years to collect them.
It is achievable but there are many other ideas to exploit an IACT for 10 years.
As a result only a survey of the galactic plane has been performed (HESS, about 1000 deg2). Adding all pointing observations, we may have explored ~5% of the sky.
What is in the other 95% of the sky? Active galaxies, off-plane galactic sources, dark matter clumps? It’s becoming a must to make a Full sky survey in VHE.
What it’s more, the VHE sky is changing all the time, so we would need to repeat the survey for a few years and we’d very much like to monitor it every night.

## Slide 4: Eg<10-100 GeV: space based surveys
Fermi-LAT
Taking data since 2008, scans full sky every 3h.
Has discovered thousands of sources.
Very small collection area for >10 GeV observations.
Energy range: max <100 GeV.
Angular resolution ~0.1° i.e. as good as IACTs.
No obvious replacement for Fermi-LAT in the future (>2020?)

## Slide 5: Eg>1 TeV: surveys with non-IACTs
HAWC
Just started to take data
Fully operative from 2014. Sierra Negra, Mexico (19°N, 97°W).
~10-15x more sensitive than Milagro.
Angular resolution ~1°.
Hadron rejection poorer than IACTs, i.e. worse sensitivity
Energy range: >1 TeV.
Larger: HiSCORE in Russia, LHASSO in China, under construction, but targeting much higher energies

## Slide 6: The archetypal wide FOV telescope: the Schmidt telescope
Radius of curvature=R
Focal length=R/2
ray
Radius of sphere=R
How to build a Schmidt:
STEP 1. Start with a spherical mirror. It has aberrations but only spherical aberrations.

## Slide 7: The archetypal wide FOV telescope: the Schmidt telescope
Radius of curvature=R
Focal length=R/2
ray
Radius of sphere=R
STEP 2. Make the focal plane spherical, with center at center of mirror. All incident directions become equivalent.

## Slide 8: The archetypal wide FOV telescope: the Schmidt telescope
STEP 3. As rays hit further and further away from optical axis, they get more a more defocused.

## Slide 9: The archetypal wide FOV telescope: the Schmidt telescope
STEP 3. As rays hit further and further away from optical axis, they get more a more defocused. Add a “stop”.

## Slide 10: The archetypal wide FOV telescope: the Schmidt telescope
Focal length=R/2
STEP 3. Considering all incident directions: where shall we place the “stop”?
At the mirror’s center of curvature, so that all directions remain equivalent.
Sphere radius R

## Slide 11: The archetypal wide FOV telescope: the Schmidt telescope
STEP 4. Add the “world-famous” Schmidt corrector plane at the stop. That eliminates spherical aberrations.

## Slide 12: The archetypal wide FOV telescope: the Schmidt telescope
Well, let’s build a “Schmidt IACT”!
This has been proposed: Mirzoyan & Andersen, APP 31 (2009) 1, with D=7m mirror, FOV ø=15°, f/D=0.8, PSF RMS=1 arcmin.
Unfortunately:
  For the corrector plate they propose a 7m ø PMMA Fresnel lense of 17mm max thickness: challenging!
  It has chromatic aberration (yeah, it’s a lens!)

## Slide 13: De-construct a Schmidt
4. Add the “world-famous” Schmidt corrector plane at the stop. That eliminates (first order) spherical aberrations.
We live with the aberration because IACT require poor optics

## Slide 14: De-construct a Schmidt
STEP 3. As rays hit further and further away from optical axis, they get more a more defocused. Add a “stop”.
Implement it placing a “light concentrator” on each of the pixels
This effectively defines D

## Slide 15: No limit to field of view!?!
Since there is no physical stop the aperture does not decrease as we go further and further off-axis. So we can go to any off-axis angle…. as long as we can pay for the mirror!

## Slide 16: Or maybe yes…
A limit is set by the shadowing of the camera on the mirror.
Here is an example:
  D=12 m, f=17 m (f/D=1.42), circular camera
   Smirror=113 m2. Plate scale=300 mm/deg
FOV ø (°) | Scam (m2) | On-axis shadowing
5 | 1.77 | 1.6%
10 | 7.1 | 6.3%
15 | 16.0 | 14%
20 | 28.4 | 25%
25 | 44.4 | 40%

## Slide 17: Solution: a non-circular camera
30°
x
z
2.5°
y
z
Shadowing = 4.4%

## Slide 18: MACHETE= Meridian Atmospheric CHErenkov Telescope
Spherical shape (through spherical facets following general spherical shape)
Camera: rectangle of 60° (following the meridian, from south to north) x 5°.
2x

## Slide 19: Field of view
Instantaneous (300 deg2)
Field of View (FOV) of a typical IACT (HESS ~20 deg2, CTA-SCT~50 deg2)

## Slide 20: Don’t move telescope! Let the sky move!
The whole sky = 42000 deg2
One year (~20000 deg2)

## Slide 21
45 m
15 m
MACHETE: the actual size
you
17 m

## Slide 22
45 m
15 m
17 m
MACHETE: the actual size
you

## Slide 23: Performance
Submitted to Astroparticle Physics
Sensitivity:
1yr survey better than HAWC 5yr survey.
Reaches 0.55% crab after 5 year survey. Similar to planned CTA 1000h survey.
1 night sensitivity: 8% crab.
Angular resolution: 0.1° (standard IACT, much better than HAWC)
Spectral resolution: 20-15% crab (standard IACT, much better than HAWC)

## Slide 24: Physics with MACHETE
A survey of half of the sky:
  New Active Galactic Nuclei.
  New galactic sources, especially if built in the south.
Monitor bright VHE sources:
  Unbiased light curves of AGN and galactic sources.
  Establish unknown duty cycles (e.g. IC-310).
  Trigger CTA and other telescopes.
The unknown:
  “Dark sources” = sources emitting only in VHE.
    Hadronic AGNs
    Dark matter clumps?
  New types of transients.

## Slide 25: Credits

## Slide 26: Backup

## Slide 27: Sky accessible by MACHETE
Every object in ~half of the sky drifts through the camera of MACHETE.
In one year we integrate ~15 hours for every source.
Sources in ~¼ sky spend about 20 minutes every night on the FOV of the telescopes: search for daily variability for sources and issue triggers to pointing IACTs like MAGIC, CTA etc.

## Slide 28: Can we make an IACT with a much wider FOV?
The most popular optics for IACTs are:
Facet radius of curvature=R
Focal length=R/2
Spherical reflector shape, with spherical facets
parallel to the sphere:
Too strong spherical aberration
Parabolic reflector shape, with spherical facets
parallel to the parabola:
No spherical aberration, no aberration for small off-axis angle, but coma for large off-axis. Good timing.
ray
ray
Facet radius of curvature=R
Focal length=R/2
Facet radius of curvature=2*R
Focal length=R
ray
Radius of sphere=R
Radius of sphere=R
Davies-Cotton, with spherical facets
not parallel to the sphere, but pointing at 2*R:
Moderate aberration at all off-axis angles. Worse timing.

## Slide 29: Can we make an IACT with a much wider FOV?
The most popular optics for IACTs are:
Facet radius of curvature=R
Focal length=R/2
Spherical reflector shape, with spherical facets
parallel to the sphere:
Too strong spherical aberration
Parabolic reflector shape, with spherical facets
parallel to the parabola:
No spherical aberration, no aberration for small off-axis angle, but coma for large off-axis. Good timing.
ray
ray
Facet radius of curvature=R
Focal length=R/2
Facet radius of curvature=2*R
Focal length=R
ray
Radius of sphere=R
Radius of sphere=R
Davies-Cotton, with spherical facets
not parallel to the sphere, but pointing at 2*R:
Moderate aberration at all off-axis angles. Worse timing.
MAGIC, HESS-II, LST
VERITAS, HESS-I, MST

## Slide 30: Can we make an IACT with a much wider FOV?
MST:
Pretty large FOV ø=7°.
Davis-Cotton mount with f=16 m, D=12 m (f/D=1.35).
Pixel size=0.18°.
PSF: r80%= 0.015° on-axis going up to 0.07° for off-axis=2.8°. Beyond that off-axis angle, PSF grows fast.

## Slide 31: Optical parameters
 | D=12m, f=17m, f/D=1.42
Plate scale | 300 mm/deg
PSF r80% | 0.07° for whole FOV (MAGIC: 0.07°on-axis —0.16° at 1.8° off-axis, MST: 0.02°on-axis —0.07° at 2.8° off-axis)
øpix=2r80% | 0.14° = 42 mm
Total mirror surface | 619 m2
Mirror surface viewed by a pixel | 113 m2
Camera FOV | 60° × 5° = 300 deg2
Number pixels | 20 000
On-axis shadowing | 4.4%
Dtmax | 3 ns
I’ve optimized some of these parameters using the ray-tracing program ZEMAX and used it to calculate the PSF (which btw is not gaussian)

## Slide 32
60° : 500 pixels : 18m
5°
40 pix
1.5m
Camera

## Slide 33
60° : 500 pixels : 18m
5°
40 pix
1.5m
Camera
Showers have a typical size ~<1°, so we only need to read out a small fraction of the camera (2°x2° = 256 pixels?).
A fast local trigger identifies those channels and selects a Region of Interest (RoI).
We use an “electronic switch” to connect the RoI to a limited number of fast digitizers.

## Slide 34
Use your imagination
This was just an example of an innovative technical solution which can be applied to this telescope. There are many others, because it is a very unconventional design. Just to mention a few:
Weight is not so much an issue because the telescope doesn’t move: we could go for copper cables and digitize far from the camera (internet cables reaching 100 m are now available).
Mirrors have no strong weight limitations. One can go much cheaper by using heavier technologies like a thick glass blank (<~1000 €/m2).
The mirror facets probably need to be realigned once every over 5-10 years, but how do you align them at all (LEDs hanging from a crane, photogrammetry?).
We need light concentrators with a sharp angular response function. Winston Cones? We would actually benefit from higher concentration (going to solid concentrators?)
PMTs are prohibitively expensive and only SiPM hold a promise to go <1 $/mm2. When? Can we play any tricks like the “light trap”?

## Slide 35: Cheap?
If MACHETE is too expensive, we just wait for standard IACTs like CTA to do the survey. Can we make it cheap enough so that it’s competitive?
Good: no need for steering mechanics, hardly any moving parts, mirrors or camera can be heavier.
Bad: 20000 pixels per telescope. 2.6 M€/telescope only for the pixels (assuming 1 $/mm2).
All in all I estimate ~10 M€ for two telescopes.
Compare to MSTs: for 10 M€ you can only build 5. Are 5 MSTs better than a 2-telescope MACHETE when it comes to surveying half of the sky? We need to know the sensitivity of MACHETE and that’s something for the next seminar.

## Slide 36: SiPMs for Cherenkov astronomy
SiPMs are the future (everyone claims), but right now they have problems. Only to mention a few:
  Crosstalk, afterpulses and dark current.
  Still expensive: target is 1 $/mm2, but right now factor 3-5 more.
  PDE (photon detection efficiency) already good at blue (400-500 nm, KETEK: 60%) but not very good at UV (<300-400 nm, ~30%).
  PDE is too good >500 nm! (KETEK: 50% at 500 nm, 30% at 600 nm), where there’s little Cherenkov but lots of NSB.
  Not available in size>9x9 mm2. Size>1.5x1.5 mm2 very expensive. For an IACT with ø>10 m a pixel is typically >100 mm2.