## Slide 1
CEPC booster and damping ring studies in EDR
Dou Wang (IHEP)
on behalf of CEPC AP group
The 2025 European Edition of the International Workshop on CEPC, 16-19 June 2025, Barcelona, Spain

## Slide 2: Content
EDR progress of CEPC Booster
  Feasibility study of the combined dipole magnets
  Progress of beam loading study
  Progress of polarization study
EDR progress of CEPC positron damping ring
  DR TDR design status
  Polarized DR study
  TF design status -- LPA multi-function ring
CEPC timing issue and detector performance
Summary

## Slide 3
CEPC layout and injector chain
30 GeV linac provides electron and positron beams for booster.
Top up injection for collider ring ~ 3% current decay
Booster is in the same tunnel as collider ring, above the collider ring, bypass in IRs (same circumference).
Budget for transfer efficiency 90%: 95% for booster + 95% for transport lines (inj. to collider).
Beam current threshold in booster is limited by RF system.
Feedback systems (Transverse & longitudinal) are need to damp the instability at low energy.
100km
30GeV
30180GeV
2 RF stations
2 Inj. (Linac to Booster)
2 Inj. (Collider to Booster)
4 Ext. (Booster to Collider)
2 Ext. (Booster to Dump)

## Slide 4: Booster TDR parameters
Injection
Extraction
*Diameter of beam pipe is 56mm for re-injection with high single bunch current @120GeV.
Energy: 30GeV  180GeV
Lower emittance ─ new lattice (TME)

## Slide 5: Booster TDR optics
Arc: TME like structure (cell length=78m)
Interleave sextupole scheme
Emittance@120GeV=1.26nm
D. Wang, C. H. Yu, D. H. Ji, Y. M. Peng, X. H. Cui,…
Arc cell
Overall idea: uniform distribution for the Q
Combined magnet (B+S) scheme + 100 sextupoles
Phase advance/cell: 100 (H) / 28 (V)
Dispersion sup.
Straight cell
Ref: D. Wang, et al., “Low emittance optics design for CEPC booster”, NIMA, 1062 (2024) 169159.
pure dipole
dipole-SF
dipole-SD

## Slide 6
Booster error setting and correction in TDR
 | Dipole | Quadrupole | Sextupole
Transverse shift X/Y (μm) | 100 | 100 | -
Longitudinal shift Z (μm) | 100 | 150 | -
Tilt about X/Y (mrad) | 0.2 | 0.2 | -
Tilt about Z (mrad) | 0.1 | 0.2 | -
Nominal field | 1e-3 | 2e-4 | 1e-3
 | Accuracy (um) | Tilt (mrad) | Gain | Offset w/ BBA(um)
BPM(10Hz) | 0.1 | 10 | 5% | 30
D. H. Ji
dipole | quadrupole
B1/B0  210-4 | 
B2/B0  510-4 | B2/B1  310-4
B3/B0  210-5 | B3/B1  210-4
B4/B0  810-5 | B4/B1  110-4
B5/B0  210-5 | B5/B1  110-4
B6/B0  810-5 | B6/B1  510-5
B7/B0  210-5 | B7/B1  510-5
B8/B0  810-5 | B8/B1  510-5
B9/B0  210-5 | B9/B1  510-5
B10/B0  810-5 | B10/B1  510-5
Include multipole errors
(100 seeds)
(93 seeds)
Residual errors after correction with 100 random seeds
Gaussian distributions are used for the errors, and they are truncated at 3σ.

## Slide 7: Booster DA with error correction & SR
The definition of beam stay clear region at different energies
TDR error setting meet the requirement of beam dynamics.
30GeV
45GeV
80GeV
120GeV
180GeV
Ref: D. Wang, et al., “Low emittance optics design for CEPC booster”, NIMA, 1062 (2024) 169159.
D. Wang, D. H. Ji

## Slide 8: Booster DA with Eddy current effect
Max K2=0.000029 (m-3)
Dedicated ramping curve to control the maximum K2.
K2 reaches max at 45GeV.
Dynamic chromaticity is not corrected.
Al beam pipe (round shape)
- inner diameter: 56mm, thickness: 2mm
Analytical estimation for eddy effect*
*Yuan Chen et al., Analytical expression development for eddy ﬁeld and the beam dynamics eﬀect on the CEPC booster, IJMPA, Vol. 36, No. 22 (2021) 2142010
Dou Wang, Yuemei Peng, Daheng Ji
Tracking DA at 45 GeV with SR, error, and eddy current
- Show the worst case

## Slide 9: Error study for polarization scheme in EDR
Orbit Correction + Horizontal dispersion
  Response Matrix
  2-level iteration：
    1st Loop: 20%~100% Corrector
    2nd Loop：30%~80% Singular Value
  Dispersion correction
  Energy adjustment by corrector
  80um RMS in both plan
Optics correction
  RM + LOCO
  Based on 30GeV simulation
  All quadrupole independent
  Dispersion correction included
Coupling and vertical dispersion correction
  Mainly used for the simulation of beam polarization. (Z. Duan)
  Skew quadrupole magnets are arranged in both the dispersion free section and the arc section to correct coupling and vertical dispersion independently.
  the coupling control target being better than 0.5%
RMS@30GeV | X | Y
Orbit (mm) | 0.080 | 0.080
Beta Beating(%) | 0.8 | 0.38
Δ Dispersion(mm) | 2.7 | 3.5
  #BPM~2400
  #Corrector~1200
Daheng Ji

## Slide 10
Careful model for combined dipoles by APES
APES: Accelerator Physics Emulation System
Particles trajectory is a curve.
The sext. center is a line along the center of the dipole.
The off-center trajectory will introduce extra quadrupole field and beta oscillation.
The position of sext. center is optimized with zero integrated quatrupole field.
Closed orbit in the combined dipole
W/O optimization
W. optimization
The 2025 European Edition of the International Workshop on CEPC
Weibin Liu, Yuan Zhang, Dou Wang

## Slide 11: Booster dipole mass production preparation in EDR
All the booster dipole magnets including the combined dipoles will be produced by the automatic fabrication lines in order to reduce the cost.
Three fabrication lines will be required to produce the required 15,000 dipole magnets within 5 years (4 dipole magnets per day).
Production error: combining machining error, assembly error,
welding deformation, lifting deformation
BST-63B: booster pure dipole; BST-63B-SF: dipole-SF combined magnet; BST-63B-SD: dipole-SD combined magnet.
Y straightness along z=0.2 mm
X straightness along z=1.5 mm
Wen Kang, Zhihui Mu

## Slide 12: Alignment scheme for the combined dipole in EDR
The booster dipole-sextuple combined magnet alignment will be based on its integrated sextupole center.
Align the combined magnet to the position where the integral of the quatrupole magnetic field along the particle’s trajectory is zero.
The alignment scheme based on mechanical center will be adopted.
 | Transversal X/mm | Vertical Y/mm | Roll z /mrad | Pitch x /mrad | Yaw y /mrad
Based on mechanical center | 0.1 | 0.102 | 0.29 | 0.019 | 0.019
Based on magnetic center | 0.407 | 0.408 | 0.29 | 0.023 | 0.023
The integrated sextupole center is moved to outside of the beam inlet/outlet points (offset: ~140 um).
Arc deviation
Xiaolong Wang

## Slide 13: Dipole (D+S) error tolerance study in EDR
The transverse offset error of the combined dipoles were scanned with100um (RMS), 300um (RMS), 400um (RMS) and 500um (RMS) to see the tolerance from the view of beam dynamics, while all the other errors keep same as TDR error table.
After horizontal closed-orbit correction, the orbit RMS is approximately 100~200 μm. When the misalignment of the combined magnet exceeds this level, the feed-down effect of the beam in the sextupole field increases more significantly, leading to larger optics errors in the corrected beam.
The combined dipole magnets were shifted Integrally without inner distortion.
Both dynamic aperture and emittance growth are checked after error correction.
Assume the error is Gaussian distribution, and are truncated at 3σ.
Dynamic aperture was tracked by SAD.
Emittance was calculated by both SAD and AT.
Daheng Ji, Dou Wang

## Slide 14: Booster DA results@30GeV
100um
300um
Maximum integral transverse offset of whole magnet: 1.5mm (rms: 500um)
500um
400um
30 GeV is the most critical energy among other energy modes according to TDR study.
Daheng Ji, Dou Wang

## Slide 15: Emittance growth @120GeV
Emittance growth at extraction energy should be controlled to make sure the injection efficiency to collider ring.
Horizontal emittance growth is very small.
Vertical emittance growth can be controlled by 8 skew quadrupoles and vertical dispersion correction.
Trans. offset of com. Dipole (RMS) |  | 100um | 300um | 400um | 500um
Hor. Emit. growth (%) |  | <0.5 | <0.8 | <1.5 | <2
Coupling (%) | w/o coupling correction | 0.59 | 0.98 | 1.24 | 1.30
Coupling (%) | w coupling correction |  | 0.57 | 0.89 | 1.08
- Coupling design goal:  1%
Daheng Ji, Dou Wang

## Slide 16: Comparison between requirements and achievement
Requirements from accelerator physics
Offset of Integrated sextupole center (RMS):  150um (Horizontal) / 150um（Vertical)
Magnet straightness along z (MAX):  1.5mm（Horizontal) / 1.0mm（Vertical)
Status of magnet production
Magnet straightness along z (MAX):  1.5mm（Horizontal) / 0.2mm（Vertical)
Status of alignment/installation
Offset of Integrated sextupole center (RMS):  100um (Horizontal) / 102um（Vertical)

## Slide 17: Booster ramping & injection scheme
3 cycles/beam
tt
Higgs
W
Z
1 cycles/beam
1 cycles/beam
1 cycles/beam
7.1s
7.1s
0.35s
4.3s
4.3s
2.7s
12.97s
2.4s
2.4s
19.9s
19.9s
19.9s
4.3s
4.3s
2.7s
4.7s damping
off-axis
on-axis
0.035s
0.27s
1.3s
0.05s
0.35s+7.1s+0.035s+7.1s=14.6s
2.7s+4.3s+4.7s+4.3s=16.0s
12.97s+2.4s+1.3s+2.4s=19.1s
(19.9s+1.0s+0.05s+1.0s)*3=65.9s
Dou Wang, Xiaohao Cui
1.0s
1.0s
1.0s
1.0s
On-axis injection @Higgs

## Slide 18: RF ramping curve
Different RF ramping curve for each energy mode (constant s )
Max RF voltage @tt determined by longitudinal quantum lifetime & DA.
s for tt: 0.14
s for Higgs: 0.094
s for W & Z: 0.088
RF: ~ 12 
VRF (180GeV)=9.8GV
W &Z
Higgs
tt
D. Wang, J.Y. Zhai

## Slide 19: RF beam loading effect @ 30 GeV
The radiation dampping rate at 30 GeV is only 0.67 Hz.
The dampping rate with bunch by bunch feedback is 8 Hz.
We are looking at two figures of merit at detune freuquency optimized for top energy:
  The growth rate of -1 mode;
  The power requirement at given detune.
Growth rate = 3.7 Hz
Pg = 1.14 MW
df = -752 Hz
Growth rate = 0.88 Hz
Pg = 0.61 MW
df = -216 Hz
Growth rate < 0.01 Hz
Pg = 0.095 MW
df = -19.4 Hz
Higgs
W
Z
Transient beam loading due to half filled ring in Higgs mode.
Higgs
Higgs
T. M. Xin, J. Y. Zhai
Mode | Growth rate [Hz] | Power required [MW] | Power Available [MW]
Higgs | < 0.01 | 0.095 | 2.40
W | 0.88 | 0.61 | 1.15
Z | 3.7 | 1.14 | 0.64
Z with df = -840 Hz | 4.6 | 0.60 | 

## Slide 20: Transient Beam Loading during the on-axis Injection @ H
During the on-axis injection process in Higgs mode, 7 to 13 large bunches will be back injected from the Storage ring;
The change of beam pattern will cause different transient phase slip compare to the normal half fill pattern (Doubled total phase slip between head and tail and jumps between the small trains);
After several synchrotron oscillations, the large bunch will be completely merged with the small existing bunches. Then the large bunches will be injected into the storage ring again;
The bunch pattern again will change because of the vacancies and a new transient phase pattern will occur.
No apparent instability detected during the whole process.
Before
During
After
T. M. Xin, J. Y. Zhai

## Slide 21: Beam Loading Study Plan in EDR
Check rest of the parts in the full cycle:
  Confirm the phase stability during the rampping process;
  Estimate the thermal load and tuning requirement;
  Investigate the solution for the possible power shortage in Z mode;
Run the full cycle simulation
Injection from the LINAC
Energy rampping
Injection into the Storage Ring
Back injection from the Storage Ring
Replenish the Storage Ring.
checked
not yet
Legend:
T. M. Xin, J. Y. Zhai

## Slide 22: Progress of polarization study in EDR
The TDR lattice suffers from superstrong resonances before Z energy
  Injected vertical emittance 6.5nm -> Polarization trans. ~ 50% @ Z & W, 20% @ Higgs
  Injected vertical emittance 1.5 nm -> Polarization trans. ~ 80% @ Z & W, 30% @ Higgs
Potential optimization:
  Move the location of superstrong resonances
  Mitigation of imperfection resonances
    Reduce lattice sensitivity
    Harmonic spin matching & partial snakes
TDR bare lattice
Intrinsic resonance
TDR lattice (one seed)
Imperfection resonance
Z. Duan

## Slide 23: Content
EDR progress of CEPC Booster
  Feasibility study of the combined dipole magnets
  Progress of beam loading study
  Progress of polarization study
EDR progress of CEPC positron damping ring
  DR TDR design status
  Polarized DR study
  TF design status -- LPA multi-function ring
CEPC timing issue and detector performance
Summary

## Slide 24: DR parameters in TDR
 | DR V3.0
Energy (Gev) | 1.1
Circumference (m) | 147
Number of trains | 2 (4)
Number of bunches/trian | 2
Total current (mA) | 12.4 (24.8)
Bending radius (m) | 2.87
Dipole strength B0 (T) | 1.28
U0 (kev/turn) | 94.6
Damping time x/y/z (ms) | 11.4/11.4/5.7
Phase/cell (degree) | 60/60
Momentum compaction | 0.013
Storage time (ms) | 20 (40)
0 (%) | 0.056
0 (mm.mrad) | 94.4
injection z (mm) | 4.4
Extract z (mm) | 4.4
inj (mm.mrad) | 2500
ext x/y (mm.mrad) | 166(97)/75(3)
inj /ext (%) | 0.18 /0.056
Energy acceptance by RF(%) | 1.8
fRF (MHz) | 650
VRF (MV) | 2.5
Longitudinal tune | 0.0387
Damping with reversed bending magnet
4 (max. 8)-bunch storage, storage time:20 (40) ms
Emittance: 2500 166/75 (97/3) mm.mrad
Flexibility for extr. emittance

## Slide 25
Phase/cell: 60/60
Interleave sextupole scheme
2 sex. families
DR optics and error study
Cell length: 3m
B=1.28T
r /0=0.355
Arc
B=1.28T
-r
0
Error study

## Slide 26: Alternative design for the DR with polarization
Produce polarized positron beam for the purpose of energy calibration @ Z & W*.
Compatible with standard top up operation
10 min storage  ~20% polarization
Asymmetric wigglers
B+=1.8T=5 B-
cell length=1.5m
16 wigglers
Wiedemann, Particle Accelerator Physics, 4 Edition
Z. Duan, D. Wang
arc
wiggler
DR V4.0 | unpolarized e+ | polarized e+
Energy (Gev) | 1.542 | 
Circumference (m) | 145 | 
Number of trains | 2(4) | 
Number of bunches/trian | 1(2) | 
Total current (mA) | 12.4 | 
Bending radius (m) | 3.44 | 
Dipole strength B0 (T) | 1.5 | 
Wiggler strength B+ (T) | 1.8 | 
Wiggler cell length (m) | 1.5 | 
U0 (kev/turn) | 190.9 | 
Damping time x/y/z (ms) | 7.77/7.77/3.89 | 
Momentum compaction | 0.015 | 
Storage time | 20 ms | 10 min
0 (%) | 0.072 | 
0 (mm.mrad) | 138 | 
injection z (mm) | 6 | 
Extract z (mm) | 5.7 | 5.6
inj (mm.mrad) | 2500 | 
ext x/y (mm.mrad) | 150/15 | 138/14
inj /ext (%) | 0.18 /0.072 | 
RF acceptance (%) | 1.8 | 
fRF (MHz) | 650 | 
VRF (MV) | 3.95 | 
Longitudinal tune | 0.044 | 

## Slide 27: Positron damping/polarizing ring
Optimization of a dual-purpose design
  Bunches stay ~ 20 msec for regular refill
  Bunches stay ~ 10 min to accumulate > 20% polarization for resonant depolarization in the Colliders
Cost and benefit comparison between two schemes
  Higher beam energy without asymmetric wigglers
  Lower beam energy with asymmetric wigglers
Asymmetric wigglers
Z. Duan

## Slide 28
PBA TF based on LPA + Storage Ring
A proposed TF
e+/e- injection @200MeV
~ 1nC in the ring for e+ and e-  off-axis injection
Multi bunch storage
Ring circumference: ~ 100 m
A demonstration for CEPC DR
The 2025 European Edition of the International Workshop on CEPC
Wei Lu, Dazhang Li, Dou Wang, Zhe Duan , Shiyu Zhou, Cai Meng, Xiaohao Cui, Jinhui Chen…

## Slide 29: Design status of the multi-function ring
60°/60° FODO
Off-axis injection with two kickers
Spin rotator longitudinal polarization
8 skew quads
Undulator parameter
Bmax: 1 T
L_cell: 25 mm
L_total: 1.6 m
Undulator
DA @ 200MeV

## Slide 30: Parameters of the multi-function ring
DR V2.0 | 200MeV | 500MeV | 1.2GeV
Circumference (m) | 100.3 |  | 
Number of bunches | 1 ~ 4 |  | 
Bunch charge (nC) | 0.001~ 1.0 | 0.1~2 | 1~ 2
Bending radius (m) | 2.65 |  | 
Dipole strength B0 (T) | 0.2517 | 0.629 | 1.51
U0 (kev/turn) | 0.053 | 2.09 | 69.3
Damping time x/y/z (s) | 2.4/2.4/1.2 | 0.157/0.157/0.079 | 0.011/0.011/0.0056
Injection time (min) | 83 (positron) | 0.3 (electron) | 
Polarization build-up time (h) | 9421 | 96.5 | 1.21
Momentum compaction | 0.04 |  | 
Storage time (s) | >8 | >0.6 | >0.04
0 (%) | 0.011 | 0.027 | 0.064
0 (mm.mrad) | 2.147 | 33.6 | 463.8
0 (nm) | 5.49 | 34.3 | 197.5
injection z (um) | 2000 | 5 | 
Natural z (mm) | 0.6 | 2.05 | 7.27
inj (mm.mrad) | 2500 | 10 | 
ext x/y (mm.mrad) | 2.2/0.2 | 34/3.4 | 464/46
inj /ext (%) | 2.0 /0.01 | 1/0.03 | 0.064
RF acceptance (%) | 3.27 | 2.45 | 1.63
fRF (MHz) | 500 (650) |  | 
VRF (MV) | 2.16 | 2.97 | 3.24
Longitudinal tune | 0.105 | 0.077 | 0.052
Plan & schedule:
Dec. 2025: acc physics design finish
Jul. 2026: construction start
Jul. 2027: electron accumulating
Dec. 2027: see the first light
Jul. 2028: positron accumulating
Dec. 2028: polarization study
The 2025 European Edition of the International Workshop on CEPC

## Slide 31: Content
EDR progress of CEPC Booster
  Feasibility study of the combined dipole magnets
  Progress of beam loading study
  Progress of polarization study
EDR progress of CEPC positron damping ring
  DR TDR design status
  Polarized DR study
  TF design status -- LPA multi-function ring
CEPC timing issue and detector performance
Summary

## Slide 32: CEPC frequency choice
CEPC: greatest common divisor=130 MHz
Min bunch spacing @ rings: 7.6923ns
Bunch spacing @ Z: 7.6923×3=23.0769 ns
FCC: greatest common divisor=400 MHz
Min bunch spacing @ rings: 2.5 ns
f (MHz) |  | SHB1 | SHB2 | Linac_S | DR | Linac_C | Booster | Collider
CEPC | Baseline (thermal cathode gun) | 158.89 | 476.76 | 2860 | 650 | 5720 | 1300 | 650
 | Alternative (RF gun) |  |  | 2860 | 650 | 5720 | 1300 | 650
*D. Wang, et al, “Problems and considerations about the injection philosophy and timing structure for CEPC”, International Journal of Modern Physics A， Vol. 37, (2022) 2246006.

## Slide 33: Bunch structure in Booster
tt
H
W
Z
35 bunches
268 bunches
1297 bunches
3978 bunches
Train structure @Z
51 train
78 bunch/train

## Slide 34: Bunch structure in Collider
tt
H
W
Z
35 bunches
268 bunches
1297 bunches
11934 bunches
Train structure @Z
153 train
78 bunch/train

## Slide 35: TDR Bunch Structures and Circumference
The spacings between adjacent bunches in any CEPC operation mode are integer numbers of 23.08 ns..
The master CEPC clock will be provided by the accelerator to the detector system(s), synchronous to the beam. The CEPC detector system relies on the clock to sample physics signal at the right time.
It is agreed to have the detector frequency of 43.3 MHz = 130 MHz / 3 = 1 / 23.08 ns, which is reasonably good from the detector point of view.
The CEPC collider ring have possible 14,442 bunch positions (14,442  23.0769 ns  c = 99.914 km).
SR 30 / 10 MW | H | Z |  | W | 
SR power per beam [MW] | 30 | 30 | 10 | 30 | 30
Bunch number | 268 | 11,934 | 3,978 | 1,297 | 35
Bunch spacing* [ns] | 576.9 | 23.1 | 69.2 | 253.8 | 4523.1
[  23.08 ns ] | 25 | 1 | 3 | 11 | 196
Train gap [%] | 54 | 17 | 17 | 1 | 53
Luminosity/IP [1034cm-2s-1] | 5.0 | 115 | 38 | 16 | 0.5
SR 30 / 10 MW | H | Z |  | W | 
SR power per beam [MW] | 30 | 30 | 10 | 30 | 30
Bunch number | 268 | 11,934 | 3,978 | 1,297 | 35
Bunch spacing* [ns] | 576.9 | 23.1 | 69.2 | 253.8 | 4523.1
[  23.08 ns ] | 25 | 1 | 3 | 11 | 196
Train gap [%] | 54 | 17 | 17 | 1 | 53
Luminosity/IP [1034cm-2s-1] | 5.0 | 115 | 38 | 16 | 0.5
SR 50 MW | H | Z | W | 
SR power per beam [MW] | 50 |  |  | 
Bunch number | 446 | 13,104 | 2,162 | 58
Bunch spacing* [ns] | 346.2 | 23.1 | 138.5 | 2700.0
[ 23.08 ns ] | 15 | 1 | 6 | 117
Train gap [%] | 54 | 9 | 10 | 53
Luminosity/IP [1034cm-2s-1] | 8.3 | 192 | 26.7 | 0.8
SR 50 MW | H | Z | W | 
SR power per beam [MW] | 50 |  |  | 
Bunch number | 446 | 13,104 | 2,162 | 58
Bunch spacing* [ns] | 346.2 | 23.1 | 138.5 | 2700.0
[ 23.08 ns ] | 15 | 1 | 6 | 117
Train gap [%] | 54 | 9 | 10 | 53
Luminosity/IP [1034cm-2s-1] | 8.3 | 192 | 26.7 | 0.8
14,442 = 2  3  29  83
It is important that beam collisions are synchronized with a 43.33 MHz clock.
D. Wang, J. C. Wang, X. H. Cui, C. Meng, G. Lei, G. Li, J. H. Chen, W. Wei…

## Slide 36: Circumference finetuning and detector performance improvement
SR 30 / 10 MW | H | Z |  | W | 
SR power per beam [MW] | 30 | 30 | 10 | 30 | 30
Bunch number | 268 | 11,934 | 3,978 | 1,297 | 35
Bunch spacing* [ns] | 553.85 | 23.08 | 69.23 | 184.62 | 3969.23
Case 14448 [  23.08 ns ] | 24 | 1 | 3 | 8 | 172
SR 30 / 10 MW | H | Z |  | W | 
SR power per beam [MW] | 30 | 30 | 10 | 30 | 30
Bunch number | 268 | 11,934 | 3,978 | 1,297 | 35
Bunch spacing* [ns] | 553.85 | 23.08 | 69.23 | 184.62 | 3969.23
Case 14448 [  23.08 ns ] | 24 | 1 | 3 | 8 | 172
CEPC will operate in the Higgs and the LL Z modes in the first 10 years.
The bunch spacing for the LL Z mode is 3×23.08 ns. If the bunching spacing for the Higgs mode is an integer number of 3×23.08 ns, e.g. 24×23.08 ns, the detector system could benefit more.
An estimation of the vertex detector using 65nm CMOS sensor shows that the power consumption per sensor chip is reduced from 310 to 165 mW, about 47% reduction. This significantly reduces the material budget, hence improve the physics performance.
SR 50 MW | H | Z | W | 
SR power per beam [MW] | 50 |  |  | 
Bunch number | 446 | 13,104 | 2,162 | 58
Bunch spacing* [ns] | 276.92 | 23.08 | 138.46 | 2584.62
Case 14448 [ 23.08 ns ] | 12 | 1 | 6 | 112
SR 50 MW | H | Z | W | 
SR power per beam [MW] | 50 |  |  | 
Bunch number | 446 | 13,104 | 2,162 | 58
Bunch spacing* [ns] | 276.92 | 23.08 | 138.46 | 2584.62
Case 14448 [ 23.08 ns ] | 12 | 1 | 6 | 112
14,448 = 24  3  7  43
D. Wang, J. Gao, J. C. Wang, X. H. Cui, C. Meng, D. P. Jin, G. Lei, J. H. Chen, Y. H. Li, W. Wei, J. B. Ye, Y. W. Wang, J. Y. Zhai, S. S. Sun, …

## Slide 37: Key milestones in EDR phase
Complete the CEPC proposal by the end of 2025
2027 (June), finish the study in EDR plan

## Slide 38: Summary
The CEPC booster/DR TDR parameter and design optimizations for all four energies (Higgs, W/Z and ttbar) have been studied. The results demonstrate that the physics design satisfies the scientific goals.
CEPC booster/DR development was reported on the TDR international review meeting (June 2023 ), cost review meeting (Sept. 2023) and 1st EDR IARC review meeting (Sept. 2024)
Feasibility evaluation of the combined dipole magnets has been carried out in EDR.
- All the dipoles are planed to be fabricated by the automatic line.
- The combined dipoles will be aligned based on the integrated sextupole center.
- Transverse alignment error(H/V): ~100 um (RMS)/102 um (RMS)
- Based on the evaluation of production error and misalignment error, the combined dipole scheme can fulfill the requirement of accelerator physics.
The timing issue of CEPC has been studied between the accelerator team and the detector team. The circumference of CEPC is slightly changed to 99955.418m to improve the detector performance.

## Slide 39: Thanks for your attention!
Welcome to suggestions and comments!