## Slide 1
ALBA Synchrotron
Accelerator Activities
Caterina Biscari
17 June 2025

## Slide 2
ALBA, the Spanish Synchrotron
National public institution, funded
50% national Government (Ministerio de Ciencia, Innovación y Universidades)
50% regional GenCat (Department de Recerca i Universitats)
User facility open to international academic and industrial communities

## Slide 3
ALBA past and future
2003 ALBA Approval
2012 Starting ALBA Operation
2021
Starting ALBA II design
2024
ALBA II project Approval
2032
ALBA II Operation
2003 – Creation of CELLS Consortium (Spanish Government and regional Catalan Government), and agreement on facility funding for the period 2003 to 2022
2023 – Addendum for 2023 funding
Governments to approve the agreement on facility funding for the period 2025-2038
2006
Starting ALBA construction

## Slide 4: ALBA 2025
Instruments for material science
XAIRA
NCD-SWEET
MISTRAL
3SBAR
NOTOS
LOREA
CLAESS
CIRCE
MINERVA
BOREAS
FAXTOR
MIRAS
MSPD
XALOC
TEM
Cryo-EM
Instruments for life science
Instruments for metrology
InCAEM
User visits
13 operating beamlines + 1 in 2027
2 electron microscopes + 1 at end of 2025
User dedicated labs
Publications
3500

## Slide 5
Chemistry and Materials Science for boosting decarbonization and decreasing material footprint
Among many others:
More performing and diverse batteries
Green energy technologies, solar and H
Low footprint materials
Catalysts for low footprint developments

## Slide 6
Electronic and Magnetic Structure of Matter for low-consumption new technologies, quantum, spintronics
Among many others:
Magnetism
Spintronic
Quantum materials
2D materials

## Slide 7
3D HOW SARS-COV-2 REPLICATES IN CELLS
ACS Nano. DOI: 10.1021/acsnano.3c07265
Life Science applications to increase life time and quality
Among many others:
Understanding diseases
Improving food quality and plant resilience
Advancing in therapies and drug development
Understanding fundamental properties of life
MISTRAL
PEST CONTROL ON CROPS
BioChar doi.org/10.1007/s42773-023-00228-8
MISTRAL

## Slide 8
ALBA as DIRECT Industrial instrument
Science and innovation programmes aligned to eliminate gaps between academic and industrial research
Special developments (i.e. on data analysis, automatization) for impact on industrial users
Harnessing a rich industrial networking (European and national projects and clusters)
Publicizing ALBA instruments towards national and international industry (outreach events)
Focusing on key industry sectors based on the strengths and opportunities of ALBA (Pharmaceutical, Steel, Energy)

## Slide 9: ALBA accelerators
Linac: 3 GHz, 110 MeV
Booster: 80 MeV to 3 GeV, 260 m,
10 nmrad emittance
Storage Ring: 3 GeV, 270 m,
4.4 nmrad emittance
500 MHz rf frequency
250 mA current
16-fold symmetry
Modified DBA lattice

## Slide 10: Operation Availability
97.4%
Along first months of 2025: Several and diverse interruptions, three of them longer than 8 hours (problems with power supplies plus blackout in whole Iberian Peninsula)
2024
2025

## Slide 11
ALBA II – our future
Upgrade of ALBA to the 4th generation
Formally approved by our governing bodies (Jan’25)
Maintain site, infrastructure and existing BLs
  New campus (labs, Data, user facilities)
  3 new BLs (2 >200 m long)
  New low emittance storage ring
  Upgrade of existing beamlines
CODI
CORUS
InnoFAB
Reach One Health
Photon flux on sample - from ALBA to ALBA II
Increase of brilliance by orders of magnitude
Increase of coherence
Advanced properties for imaging, spectroscopy, diffraction
Advanced data management

## Slide 12
Instruments for material science
XAIRA
NCD-SWEET
MISTRAL
3SBAR
NOTOS
LOREA
CLAESS
CIRCE
MINERVA
BOREAS
FAXTOR
MIRAS
MSPD
XALOC
Instruments for life science
CORUS
CALIMA
CODI
Instruments for metrology
ALBA II - Day One - 2032
New Storage Ring
TEM
Cryo-EM
InCAEM
Upgraded Beamlines

## Slide 13: Implementation  2030-2031
Long beamlines at BL02-ID , BL03-Bend, BL04-ID, BL08-ID
In 2032:
12 (out of 13) ID beamlines
4 (out of 13) Bending beamlines
1 IR beamline
1 Visible diagnostics
3 XR pinhole diagnostics

## Slide 14: ALBA II Accelerator main parameters and WPs
# | Work Packages | FTE
WP01 | Magnets | 4,5
WP02 | Vacuum | 2,0
WP03 | Pulsed | 1,0
WP04 | Girders | 1,0
WP05 | Diagnostics & Feedbacks | 1,2
WP06 | Insertion Devices | 0,1
WP07 | FEs | 0,1
WP08 | RF | 0,9
WP09 | PS | 0,1
WP10 | Electronics | 0,0
WP11 | Controls | 0,0
WP12 | IT infrastructure | 0,0
WP13 | Automation | 0,0
WP14 | Radiation Protection | 0,1
WP15 | Alignment | 0,1
WP16 | Cabling infrastructure | 0,1
WP17 | Cooling infrastructure | 0,0
WP18 | Layout & tests coordination | 0,4
WP19 | Integration | 0,8
WP20 | Optics & Beam Dynamics | 2,8
WP21 | Coordination | 0,7
 | Transversal (FEA, Drafman,…) | 3,3
TOTAL |  | 19,2
As per today, around 40 persons,
19 FTEs dedication, under the guidance of ALBA Director of Accelerators, Francis Pérez .
WEPM105, IPAC 25

## Slide 15
Emittance: 200 pm·rad (160pm·rad / 80pm·rad @50% coupling)
●Mom. Compaction: 1.1·10-4
●βx at SS: 10.0 / 2.2 / 2.3 m
●βy at SS: 6.2 / 2.2 / 2.3 m
●Tunes: 38.24 / 12.35
●Chromaticity: -96 / -39

## Slide 17: Magnets: EM prototypes
The CfT for resistive prototypes included 8 magnets divided into 4 lots.
Contract for all 4 lots was signed with 1 single company (ANTEC) on 18 Jun’24. The kick-off meeting was held on 05 Jul’24.
MAGNETS
Bending magnets | 
Lot 1 | QD
 | QDS conventional
 | QDS embedded
“quadrupoles” | 
Lot 2 | Q3
 | QF/QFS
Sextupoles | 
Lot 3 | SH
 | SV
Correctors | 
Lot 4 | CORR

## Slide 18: Design of magnets for final lattice
Layout implementation:
MAGNETS
Progress in design of magnet supports and alignment system:
  Proposal of common baseplate for Sextupole+Octupole
Shims
Positioner

## Slide 19: Next steps
Study of photon extraction lines and impact on magnets’ design.
Design of assembly strategy for PM-based magnets (QDS-PM and QD-Superbend) without yoke opening (lateral sliding or similar).
Definition of protocol together with Alignment Group in order to guarantee 30µm rms positioning accuracy.
MAGNETS

## Slide 20: Magnets: PM prototypes
Lot 1 (QDS-PM): New tuning mechanism, consisting of an adjustable gap at the yoke’s backbone, by adjustable shim plates at the ends of the magnet. This will allow an estimated cost reduction for the series magnets of ~10%.
MAGNETS
Estimated cost reduction ~10%
PM material reduced by ~28%
NiFe material reduced by ~10%
PSI
Control gap adjustment mechanism
Initial proposal (CfT)
Manufacturer’s proposal
Shim plates

## Slide 21
4 inner and 4 outer conductor rods create two opposite dipole fields powered with independent pulsed power supplies
Injection: Double Dipole Kicker
G. Benedetti et al 2023 J. Phys. Conf. Ser. 2420 012017
Inner coils field
Outer coils field
Superposition of the inner and outer coils fields
8 rods powered with independent
Zero field at the stored beam
Field peak at the injected beam
Only 4 outer rods powered
Dipole field for on-axis injection
Useful during commissioning
Notes: longitudinal field is zero on-axis and non-linear off-axis
Però narrower plateau vs NLK

## Slide 22
  @ ESRF - Longitudinal and transversal coating uniformity requirement is within 10%
  A resistance measurement system built by AVS measures the local resistance by four wire measurement.
The DDK ALBA prototype to be tested at ALBA
Collaborating with ESRF and Sirius
@ SIRIUS - being manufactured at CNPEM lab
5 ceramic chambers produced (Engecer)
First UHV flanges and Nb + Ti transition pieces produced.
First ceramics brazing expected next month
Coating technique studies are ongoing:
    Ti-sputtering of one rectangular wire w/o masks
    Wire geometry optimized to deliver a ratio coating thickness of at least 1:4
DDK chamber delivery expected by end 2025
DDK +
DDKPPS integration

## Slide 24: Prototyping BPMs

## Slide 26: Girders
Pros:
Much larger gaps between Girders.
Relatively easier for Girder installation.
Lighter Girders (~5% and ~18%) .
3x SAME magnet distribution:
  Same Top plate and complete Girder.
Cons:
3 different lengths for Girders.
1x larger Girder (~25% heavier: ~11.300 kg)
Extra supports for VC, pumps, (…)?
2.070
2.400
2.400
2.400
3.130
395
150
150
132
ALBA II Accelerator meeting
3x Different Frame
3x Different
Top plates
Division on Pumps
Length Optimization

## Slide 27
Girders

## Slide 28: Main RF system
P. Solans
Main RF high power components reused for ALBA-II.
RF main voltage must provide enough RF acceptance and redundancy in case of a cavity trip.
EU-HOM NC cavity
ALBA Main RF IOT based transmitters
Short bunches lead to small lifetimes due to high Touschek effect (for ALBA σ = ~17 ps)
Upgrade to SSPA
WR1800
Parameter | Value | Unit
Frequency | 499.654 | MHz
Number of cavities | 6 | -
Voltage | 2.4 | MV
RF acceptance | 7 | %
Loses per turn (bare lattice) | 1.028 | MeV
Transmitter power (300 mA) | 90 | kW
Momentum compaction | 9.6·E-5 | -
Synchrotron frequency* | 2.25 | kHz
Bunch length (σ)* | 6.96 | ps
Parameter | Value | Unit
Frequency | 499.654 | MHz
Number of cavities | 6 | -
Voltage | 2.4 | MV
RF acceptance | 7 | %
Loses per turn (bare lattice) | 1.028 | MeV
Transmitter power (300 mA) | 90 | kW
 | 9.6·E-5 | -
Synchrotron frequency* | 2.25 | kHz
Bunch length (σ)* | 6.96 | ps
* w/o harmonic system

## Slide 29: Harmonic RF system
An active 3rd harmonic system is foreseen in order to increase the bunch length and Touschek lifetime.
P. Solans
I. Bellafont
ALBA-II total voltage
Total voltage present a flat potential region where electrons can spread
Prototype successfully tested in BESSY-II and full system will be tested at ALBA, placed in ALBA II position

## Slide 30
Storing
SR components on arrival
Girders assembled with magnets
Spare parts, which are now in the warehouse that will be converted on Lab for testing and assembly
Assembled vacuum arcs (in the EH)
Testing, assembly and storing areas
Definition of requirements is ongoing, we expect to be able to store with minimum services.
Definition of requirements for testing and assembly is being refined.
MA
300m2
GI
550m2
MA+GI
800m2
PS
300m2
MA+GI
200m2
PS
300m2
MA
40m2
PS
150m2
ALBA & ALBA II spare parts: 400m2
ALBA spare parts 2030-32
400 m2
assembly & testing
ready for installation
storage

## Slide 31
Thank you for your attention