## Slide 1
CEPC machine protection and radiation environment studies in EDR
Guangyi Tang
On behalf of CEPC RP Group and MP Group
17 Jun. 2025, Barcelona, CEPC Workshop EU Edition

## Slide 2: Content
Radiation protection
  EDR goal and scope
  Progress in EDR stage
Machine protection
  EDR goal and scope
  Progress in EDR stage
Summary

## Slide 3: What we did in TDR
Estimate absorbed doses to booster and collider magnets and design lead shielding.
  Absorbed dose after 18-year operation
Design linac and collider dumps
Determine linac bulk shielding
Radionuclide Production
  In the air/water/tunnel wall in the linac/collider arc/dump hall

## Slide 4: EDR goal and scope: radiation protection
Environment impact assessment of CEPC proposal
  Prompt radiation estimation
    In linac, collider/booster, damping ring, transport line, collimator, RF hall, IR hall, SR hall, dump hall.
  Induced radioactivity estimation
    In linac, collider/booster, damping ring, transport line, collimator, RF hall, IR hall, SR hall, dump hall.
  Design radiation dose monitor system
  Design personal protection system
Radiation-sensitive equipment protection for CEPC
  Electronics: power supply, BPM, control system, etc.
  Optical fiber
  Cable/insulation
  Engineering design: support, cooling, …

## Slide 5: Induced dose-eq in collider tunnel, 10min after shutdown
For 4 operations (120/45.5/80/180 GeV), simulate the induced dose-eq caused by SR and random beam losses.
The dose-eq after 1-year running and 10-min shutdown is shown below
@Higgs operation：1m away from equipment <1 uSv/h，surface of equipment ~10 uSv/h
  SR random beam losses
Similar radiation level around the end of BEPCII Linac.

## Slide 6: Induced dose-eq in collider tunnel, 10min after shutdown
@Z operation: 1m away from equipment <2 uSv/h， surface of equipment ~ 20 uSv/h
  SR can be negligible
A little higher than radiation level around around the end of BEPCII Linac
@ WW operation: 1m away from equipment <1 uSv/h， surface of equipment ~10 uSv/h
  SR can be negligible

## Slide 7: Induced dose-eq in collider tunnel, 10min after shutdown
@ttbar operation： 1m away from equipment <20 uSv/h， surface of equipment >100 uSv/h
  SR random beam losses
Higher than the radiation level around BEPCII positron target.

## Slide 8: Induced dose-eq in collider tunnel, 1d after shutdown
@ttbar operation： 1m away from equipment <5 uSv/h， surface of equipment >10 uSv/h
  SR
  Slightly higher than the induced dose-eq @Z/WW operation.
All simulations are included in the environment impact assessment report.

## Slide 9: Linac & damping ring & Linac-DR transport line
Damping ring SR critical energy ~ 1 keV，negligible
Estimate
  Linac/damping ring/ L-to-DR transport line bulk shielding
  Radioactivity
Fluka setup
Linac
Damping ring
L-to-DR transport line

## Slide 10: Linac & damping ring & Linac-DR transport line
Damping ring SR critical energy ~ 1 keV，negligible
Estimate
  Linac/damping ring/ L-to-DR transport line bulk shielding
  Radioactivity
Damping ring shielding
Damping ring and transport line
concrete
concrete
Position | Thickness of the wall
Inner | 0.5m
Outer | 3.0m
Bottom | 0.5m
Top | 1.2m

## Slide 11: RF hall, transport line, etc.
The prompt radiation level and induced radioactivity are estimated.
The simulations for transport lines are also finished. The simulations for IR/SR hall are close to be finished. Will summary all results in the Environment impact assessment report.
Booster RF cavity
Collider RF cavity

## Slide 12: Radiation protection for electronics
For electronics
With a 3-leg maze, radiation in the auxiliary tunnel decreases to a safe level
Alternatively, by shielding with 20cm lead and 20cm concrete, radiation in gaps between supports decreases to a safe level.
 | Upper limit | 3-leg maze with 1m-thick concrete wall | 20-cm lead + 20-cm concrete | 15-cm lead + 15-cm concrete
High energy hadron fluence ( |  |  |  | 
Absorbed dose (Gy/y) | 20 | (1m far from entrance) | <20 | <80
1MeV equivalent neutron fluence ( |  |  |  | 
 | Upper limit | 3-leg maze with 1m-thick concrete wall | 20-cm lead + 20-cm concrete | 15-cm lead + 15-cm concrete
Absorbed dose (Gy/y) | 20 |  | <20 | <80

## Slide 13: Radiation protection for fiber, cable insulation
Upper limit for ordinary optical fiber: absorbed dose < 100 Gy/y Upper limit for radiation-resistant optical fiber: absorbed dose < 10 kGy/y
  Radiation-resistant optical fibers are safe in the inner trench with thicker-than-30-cm concrete cover and safe in the outer trench thinner-than-10-cm concrete cover.
  Ordinary optical fibers need thicker cover or deeper trench..
For cables and insulations (polyethylene): absorbed dose <1 MGy
  Use 2cm-thick 1m-high lead sheet, or 10cm-thick 1m-high concrete block to shield radiation.
 | Trench with no cover | Trench with 10-cm concrete cover | Trench with 30-cm concrete cover
inner trench | <400 kGy/y | <200 kGy/y | <40 kGy/y
outer trench | <50 kGy/y | <5 kGy/y | <300 Gy/y
Higgs
ttbar

## Slide 14: Water cooling in dipole and quadrupole
To absorb deposited energy and cool the magnet core and lead, 8 stainless-steel tubes are used.
72% deposited energy in magnets and lead can be removed. The ventilation system load has been significantly reduced.
The experiment to fix SS tubes on lead is planed.
Mei Yang and Haijing Wang

## Slide 15: TDR shielding scheme v.s. photon absorber scheme
TDR scheme：25mm lead in magnet
The power and price are almost the same
Photon absorber scheme ：38mm lead in dipole and quadrupole, extra lead cover on dipole
dipole
quadrupole
Mei Yang

## Slide 16: Beamline arrangement
TDR scheme
25mm thick lead
Photon absorber scheme
Photon absorber and lead shields
dipole
Sexto
quadru
dipole

## Slide 17: Prompt absorbed dose：@ttbar SR and Z beamloss
TDR @ttbar SR
@Z beamloss
The absorbed dose in the inner side is higher, indicating that need to optimize the lead usage.
Photon absorber scheme

## Slide 18: Induced dose-eq in collider tunnel, 10min after shutdown
TDR scheme
@ttbar SR
For TDR scheme, @ttbar operation, the induced dose-eq is higher, it is better to wait more time
@Z beamloss
@Z operation, the radiation level using TDR scheme is better.
Photon absorber scheme

## Slide 19: Content
Radiation protection
  EDR goal and scope
  Process in EDR stage
Machine protection
  EDR goal and scope
  process
summary

## Slide 20: EDR goal and scope: machine protection
Active protection: beam dumps and corresponding transport line
  The engineering design for the dumps, kickers and septum.
  Design the control system for the collider dump
Passive protection: collimation system
  Simulate the beamloss distribution under different beam loss scenarios
  Develop tools to simulate beam-collimator interaction
  Further study to understand whether MP collimators can help to control beam-induced backgrounds near the IR, combining with MDI collimators and SR masks.
  Determine the collimator parameters
  Engineering design for collimator.

## Slide 21: Design boundary conditions and Beam losses scenarios
Currently, focus on 5 beam loss scenarios:
  Superconducting RF cavities/magnets quenching, a power supply of magnets breakdown (affect 1/8 of all dipoles, or several quadrupoles, or several sextopoles)
  The fields decays according to an exponential function: . For superconducting RF cavities quenching cases: For superconducting magnets quenching cases: For magnet power supply breakdown case: turns
The bottom line of the passive protection system is to ensure that the IR is not damaged and protect all equipment except the collimators. If we did better, the collimators can be protected
  Hits and deposited energy in IR should be in a low level
  The temperature rise should be lower enough. E.g. deposited energy in one bellow should be lower than 10J

## Slide 22: Collimators setup
33 collimators for each ring (@Marseille workshop, the number is 58)
  19 MDI collimators and 2 SR masks (see Haoyu’s talk tomorrow)
  4 horizontal betatron collimators, , in the straight sections
  4 momentum collimators, , in the arc sections
  4 vertical betatron collimators, , in the straight sections
Two types: horizontal/vertical collimator
  Aperture: 3~4 mm
Material: Molybdenum – Carbon composite
x
horizontal collimator
y
x
vertical collimator
y
z
x

## Slide 23: Combine SAD and FLUKA
Different scenarios can be set in SAD simulation.
Beam losses along beam pipe/collimators will be record.
All processes that beam losses hitting collimators would pass to FLUKA simulations, then secondaries send back to SAD.
What’s new: the kicker and septum for the extraction line to collider dump are added in the SAD simulation to study the extraction efficiency.

## Slide 24: Primary results: @Z operation
One-power-supply-breakdown case: beams begin to loss after tens of turns.
  Have enough time to extract beams
Superconducting-RF-cavities-quenching case: beams begin to loss after 12 turns.
  Have enough time to extract beams, too
Superconducting-magnets-quenching case: beams begin to loss at the first turn.
  Extract nothing even though the response time of extraction line is set to be 1 turn.
For Higgs/WW/ttbar operations, the similar simulations will be finished soon.

## Slide 25: Primary results: @Z operation
SC-magnets-quenching case is the most critical one. In some region, the beamloss energy is around 1MJ.
The collimators are damaged probably, careful simulation is on the way to find out whether the downstream equipment survived or not.
The next version may be coming.
IP and beam dump
MP collimators
MDI collimators and SR masks

## Slide 26: Summary
For the environment impact assessment, all shielding designs and radiation level estimations are finished or closed to be finished
  Collider arc, Linac, damping ring, transport lines, RF hall are finished.
  IP hall and SR hall will be finished soon
Radiation-sensitive shielding design is moving forward with engineering design.
For the machine protection, more simulations for different operations are coming. The radiation level downstream collimators will be carefully studied. The collimator optimization is ongoing.
Thank you