## Slide 1
PICOSEC Micromegas: A Scalable Solution for
Precise Timing Applications
, Thomas Papaevangelou(1)
on behalf of the DRD1-PICOSEC Micromegas Collaboration
(1)CEA/IRFU/Université Paris – Saclay
Tuesday, 17th June 2025
CEPC 2025 – 2025 European Edition of the International Workshop
on the Circular Electron-Positron Collider

## Slide 2: The PICOSEC Micromegas Collaboration
AUTH (Greece) I. Angelis, K. Kordas, C. Lampoudis, I. Maniatis, I. Manthos, K. Paraschou, D. Sampsonidis, A. Tsiamis, S. E. Tzamarias
CEA-IRFU, LIST, LIDYL(France) S. Aune, D. Desforge, I. Giomataris, T. Gustavsson, F. Jeanneau, A. Kallitsopoulou, M. Kebbiri, P. Legou, T. Papaevangelou, M. Pomorski, E. Scorsonne
CERN (Switzerland) J. Bortfeldt, F. Brunbauer, C. David, D. Janssens, K.J. Floethner, M. Lupberger, M. Lisowska, H. Müller, E. Oliveri, G. Orlandini, F. Resnati, L. Ropelewski, L. Scharenberg, T. Schneider, M. van Stenis, R. Veenhof
HIP (Finland) F. Garcı́a
Jefferson Lab (USA) K. Gnanvo
LIP (Portugal) M. Gallinaro
NCSR Demokritos, (Greece) G. Fanourakis
NTUA (Greece) Y. Tsipolitis
Ruder Boškovic Institute(Croatia) : A. Utrobicic
Stony Brook University (USA) J.Datta
USTC (Hefei, China) J. Liu, B. Qi, X. Wang, Z. Zhang, Y. Zhou
University of Zagreb(Croatia) M. Kovacic
University of Pavia (Italy) D. Fiorina, M. Brunoldi, I.Vai, P.Vitulo
Univeristy of Virginia (USA) S. White

## Slide 3: What is our motivation?
Tracking challenges for HL-LHC:
      LHC will go to higher energy & luminosity
        5x nominal instantaneous luminosity  Increased particle densities
        20x current integrated luminosity  Increased radiation damage
      What are the needs:
        Reduction of mixing different events due to pile-up
        Track to vertex association  3D tracking with timing information
Timing with a few 10’s of Picosecond
      Extra detector requirements:
          Large area coverage
          Resistance to aging effects
          Multi-pad readout tracking
      Detector technologies  Mainly Solid State
  Gaseous detectors
    Resistive Plate Chambers (RPCs) (σt ~ 30 ps)
    Micro-Pattern Gaseous Detectors (σt ~ 1 ns)
Giant improvement ~ 3 orders of magnitude compared to standard MPGDs

## Slide 4: Outline
Towards an engineered PICOSEC MM module :
multiple directions in detector development
Proof of Concept
  Prove the performance in single channel prototypes
  Achieved 24 ps !
Optimization R&D
  Detector design
    Signal Integrity
  Research on alternative photocathode materials
  Scalability
    Detector & Electronics
R&D for Applications
  Two possible application scenarios ( ENUBET, Muon Collider)
    R&D Depending on application requirements
    Robustness
    Research on alternative gas mixtures

## Slide 5: The PICOSEC Micromegas Technology

## Slide 6: The PICOSEC Micromegas Technology
Y. Giomataris, P. Rebourgeard, J.P. Robert and G. Charpak, “Micromegas: A high-granularity position sensitive gaseous detector for high particle-flux environments”, Nuc. Instrum. Meth. A 376 (1996) 29
J.Bortfeldt, et al., “PICOSEC: Charged particle timing at sub-25 picosecond precision with a Micromegas based detector”, https://doi.org/10.1016/j.nima.2018.04.033
Timing limitation factor
  Stochastic nature of ionization
    Randomness of last ionization
    Time jitter of a few ns
Timing performance improvement
  Simultaneous creation of the electrons
  Minimization of the direct ionization probability
Timing MM geometry
  Smaller drift gap  eliminate ionization
    Higher electric field  eliminate diffusion
     pre-avalanche
Additional components in MM geometry
  Cherenkov radiator  replace ionization mechanism
  Solid Converter  prompt photoelectrons
      well-defined location

## Slide 7: Proof of Concept

## Slide 8: The Single anode prototype
Detector technology
  Bulk Micromegas  1cm
  The Sensor:
Crystal & Photocathode material
  MgF2 crystal (3 mm) +
  Metallic substrate (Cr) + CsI  11 p.e./track
Gas Composition
  COMPASS Gas : 80% Ne – 10% CF4-10%C2H6
V[V]
T[ns]
Electron peak
Ion tail
First timing measurement @ Particle Beam results – 2017
  Muon Beam of 150 GeV/c
  Single channel prototype :
    Drift Gap (200 μm)
J.Borteldt, et al. “PICOSEC: Charged particle timing at sub-25 picosecond precision with a Micromegas based detector”, Nuc. Instrum. Meth. A (2021)https://doi.org/10.1016/j.nima.2018.04.033
11 p.e.
Timing Resolution 
RMS of Signal Arrival Time Distribution
Record for MPGDs 24 ps !
Notes: Bulk?

## Slide 9
Optimization R&D

## Slide 10
Particle Beams @ CERN SPS H4 Beamline
  Highly energetic muons (80-150 GeV)
The Setup
  Use GEMs for tracking
  Use MCP PMTs as timing reference devices and for triggering
  Different PICOSEC Micromegas Prototypes
  Electronics: Commercial/Custom-made preamplifiers
  Digitizers – Lecroy scopes
Detector Testing - Particle beams

## Slide 11
D. Janssens, Robust photocathodes and spatial resolution studies of resistive PICOSEC Micromegas precise-timing detectors- The 8th International Conference on MPGDs https://indico.cern.ch/event/1453371/contributions/6146435/
Optimization of geometry and connectivity
Focus on Operation Stability
  Signal Integrity (different prototypes  10,13,15 mm)
      Noise reduction
      Reassembly feature
  Parasitic influence
    Capacitance and inductance
New Record
10 mm & CsI  12.5 ps
(drift gap reduced to 125μm)
    More info @  Utrobicic, A., et al. "Single channel PICOSEC Micromegas detector with improved time resolution." NIM A 1072 (2025): 170127 https://doi.org/10.1016/j.nima.2024.170127
Based on the same design
  Investigating the μRWELL technology for the amplification region
Best Result
P120-D100 & CsI  23.5 ps
 10 mm
A.Pandey. Precise Timing with PICOSEC μRWELL detector-DRD1 Collaboration Meeting https://indico.cern.ch/event/1413681/contributions/5993207/
  Investigating the spatial resolution response
Best Result
 15 mm & CsI  0.5 mm (central region)
Notes: The design overview of the single-channel PICOSEC Micromegas detector includes the following key points:
Comprehensive Design Elements: The design encompasses the detector board, the vessel, auxiliary mechanical parts, and electrical connections for high voltage (HV) and signal transmission.
Stability Improvement: The design focuses on enhancing operational stability to better utilize the detector’s capabilities and minimize issues that could arise from external factors.
Noise Reduction: Special emphasis is placed on reducing electronic noise, which is critical for maintaining the integrity of signals and optimizing timing performance.
Signal Integrity: Ensures that the detector’s design maintains signal quality, which is essential for accurate measurements and timing resolutions.
Ease of Reassembly: A streamlined assembly process is implemented, allowing for rapid replacement of detector components, which facilitates efficient testing and measurement with different configurations.
Parasitics Influence: The design takes into account the impact of parasitic capacitance and inductance on output signal integrity, making it a focus area during the design process to mitigate any potential negative effects.

## Slide 12: Photocathode Robustness
In the research of photocathode materials
  Standard photocathode: 18 nm CsI +3 nm Cr ~ 11 pe/MIP
  CsI sensitive to humidity/ion backflow & sparks
https://doi.org/10.1016/j.nima.2011.10.019
  New materials under test (B4C, DLC)
M. Lisowska, et al. – Photocathode characterization for robust PICOSEC Micromegas precise-timing detectors https://arxiv.org/abs/2407.09953
1.5 nm DLC  10 mm
31.9 1.3 ps
9 nm B4C  10 mm
34.5 1.5 ps
Depositions at different Labs
  DLC with magnetron sputtering at USTC, China
  DLC with DC magnetron vacuum deposition machine at CERN
  B4C with sputtering at CEA Saclay, France
  B4C with sputtering at ESS, Sweden
X.Wang,et al. – A Novel Diamond-like Carbon based photocathode for PICOSEC Micromegas Detectors https://arxiv.org/abs/2406.08712
3.5 nm DLC  10 mm
42.2 0.8 ps

## Slide 13: Scalability – The 10x10cm2 PICOSEC Prototypes
Rigid, ceramic-core PCB for the MM readout (CERN)
  Crystal decoupled from the MM board
   of 1cm
  First proof of concept that influenced the next generation designs
A.Utrobicic: A large area 100 channel PICOSEC Micromegas detector with sub 20ps time resolution, The 7th International Conference on Micropattern Gaseous Detectors (2022), https://iopscience.iop.org/article/10.1088/1748-0221/18/07/C07012

## Slide 14: Scalability – The 10x10cm2 PICOSEC Prototypes
Rigid, ceramic-core PCB for the MM readout (CERN)
  Crystal decoupled from the MM board
   of 1cm
  First proof of concept that influenced the next generation designs
A. Utrobicic, et al., A large area100-channel PICOSEC Micromegas detector with time resolution at the 20 ps level, JINST 18 (07) (2023) C07012. https://iopscience.iop.org/article/10.1088/1748-0221/18/07/C07012
180μm drift gap
CsI photocathode
Best timing: 16.8 0.1 ps
Uniformity of response
2.5 nmDLC photocathode
Best timing:
27.2 0.5 ps
The μRWELL PICOSEC-Micromegas Prototype (JLab)
  P120-D100 prototype with the best performance in the single channel prototype used as the basis for this design
 Best timing resolution with CsI photocathode 50 ps
Thermal Bonding method for the MM readout (USTC)
Y.Meng: PICOSEC Micromegas Precise Timing Detectors; Development towards Large-area and Integration, The 8th International Conference on Micropattern Gaseous Detectors (2024), https://arxiv.org/abs/2501.04991

## Slide 15: Scalability – The 20x20cm2 PICOSEC Prototype
Thermal Bonding method for the MM readout (USTC)
  Coating of Germanium on PCB to form the resistive anode Resistivity 50 MΩ/
  Alternative method of Micromegas construction
    Looking forward to achieve high-rate capabilities
Y.Meng: PICOSEC Micromegas Precise Timing Detectors; Development towards Large-area and Integration, The 8th International Conference on Micropattern Gaseous Detectors (2024), JINST https://arxiv.org/abs/2501.04991
Following the same principle
  Similar assembly as the 10x10 cm2
  Using (4) MgF2 crystals on a frame
  Kapton films underneath to compensate thickness variations between crystals
  The 10x10 prototype
CsI photocathode
Best timing: 25.4 0.2 ps
Notes: Basic Principle: The TBM fabricates the avalanche structure of the Micromegas detector by bonding a stretched stainless-steel mesh directly onto a readout printed circuit board (PCB). This is done using hot rollers that melt and press spacers made from a thermal bonding film, which has a triple-layer adhesive-polyester-adhesive configuration , .
Spacer Arrangement: The spacers, which support the mesh and define the micro-gap necessary for operation, are typically arranged with a diameter of less than 1 mm. They are positioned at approximately 10 mm intervals on the PCB, ensuring effective support and minimal dead space .
No Chemical Processes: Unlike traditional methods that require etching and chemical agents, TBM is an etching-free process. The adhesive layers in the spacers solidify upon cooling, fixing the mesh in place and creating the required micro-gap while avoiding the complications associated with chemical processes .
Temperature and Pressure Control: Precise control over the conditions during the thermal bonding process, particularly temperature and pressure, is crucial. The spacer materials must be fully compressed while being heated to achieve uniformity in the final structure .
Construction Process:
Heating: The thermal bonding film is heated using hot rollers to melt the adhesive layers.
Pressing: The spacers are pressed against the PCB and mesh during the heating to form a solid bond as they cool down.
Solidification: As the adhesive cools, it hardens, securing the mesh in place and forming the necessary avalanche gap.
Advantages: This method provides several advantages, including simplicity in operations, reduced equipment requirements, enhanced flexibility for designing new detector configurations, and the potential for high gain and low ion backflow , .
Overall, the thermal bonding method streamlines and enhances the production of Micromegas detectors, making them easier to manufacture while maintaining performance standards.

## Slide 16: Scalability – The Electronics
Towards a large-scale prototypes, we need to develop appropriate frond-end & back-end electronics
Discrete current preamplifiers (CEA)
  8 ch amplifier boards
  High gain >30 dB
  Bandwidth > 1GHz
RF current preamplifier (CERN/RBI)
  10 ch amplifier boards
  High gain 38.5 dB @ 100 MHz
  4 MHz<Bandwidth<650MHz
RF current preamplifier (USTC)
  16 ch amplifier boards
  25 MHz<Bandwidth<700 MHz
SAMPIC digitizer (IJCLab)
  8.5 GS/s sampling frequency
  1.6 GHz bandwidth
  Up to 128ch per single digitizer
  16-channel modules
FastIC ASIC (CERN)
  Aiming for a binary output of the SAT and signal amplitude
  8 readout channels
DRS4 based digitizer (USTC)
  5.12 GS/s sampling frequency
  950 MHz bandwidth
  Dedicated SAMTEC cables for connectivity

## Slide 17
R&D for Applications

## Slide 18: The Muon Collider Detector ( INFN, University of Pavia)
Problems to be addressed:
  High levels of background noise by muon decays
  High event rates up to to distinguish signals from background and harmful environments
  Improve track reconstruction
    Out-to-in reconstruction approach
  Aiming for 100 ps timing resolution
Main Goals : Stability, Sustainability and Durability
R&D focus:
  Eco-friendly gas mixtures
  Resilient photocathode materials
More Info @ Aimè, C., et al. "Simulation and R&D studies for the muon spectrometer at a 10 TeV Muon Collider." NIMA(2024): https://doi.org/10.1016/j.nima.2024.169903
: 75/25
Single channel  10mm & CsI
Best timing: 17.1 0.2 ps

## Slide 19: Event Triggering and Tagging Context (CEA Saclay)
Follow up on Cross-section measurements CERN NP06/ENUBET(Enhanced NeUtrino BEams from kaon Tagging)
ENUBET is aimed:
  At designing a narrow-band beam @ GeV scale
  Having control of the neutrino flux & energy
ENUBET characteristics facility
  Monitored neutrino beam with no one-to-one correlation between positrons tagged in beamline and neutrinos tagged in the far detector
The ENUBET experiment: F. Terranova, F. Acerbi, G. Ballerini, M. Bonesini, A. Branca, C. Brizzolari
https://doi.org/10.22323/1.390.0182
1
2
Sub-ns sampling would offer this correlation
  On an event-by-event basis
  Determine the flavor of neutrino
Embed a PICOSEC-Micromegas layer inside the instrumented hadron damp

## Slide 20: Detector requirements on the hadron dump
ENUBET: the first monitored neutrino beam F. Terranova https://indico.cern.ch/event/1353517/attachments/2772398/4831052/terranova_cern_enubet_15dec2023.pdf
The Setup
  8 absorbers made out of iron or rock
  8 muon detector planes
The detector technology need to cope with
  Maximum muon rate of
  Neutron fluence of
  * In the layer closer to the end of the decay tunnel

## Slide 21
  Read-out pads
  Insulating layer
  Resistive Layer : DLC
  -HV
  GND
  +HV
Robustness & Efficiency ≡ Resistive prototypes
Advantages of the resistive technology
  Elimination of destructive effects of discharges
  Stable operation in harmful environment (e.g. pions)
  Possibility to improve position reconstruction

## Slide 22
Robustness & Efficiency ≡ Resistive prototypes
Advantages of the resistive technology
  Elimination of destructive effects of discharges
  Stable operation in harmful environment (e.g. pions)
  Possibility to improve position reconstruction
The goal is to exploit these advantages while maintaining precise timing resolution
D. Janssens, PhD dissertation, https://cds.cern.ch/record/2890572
mimimum for protection
rate capability
mimimum for timing
The surface resistivity should be chosen to ensure that :
  The leading edge of the signal is minimally affected by the delayed component
  The estimated rate capability
  The protection against discharges

## Slide 23
Detector R&D for the resistivity value
  Beam
    Muon's energy (80-150 GeV)
    8 cm diameter of beam
    muons/spill (measured rate ~ kHz/)
Multi-Pad Prototype (7-pad)
  200 kΩ,10 MΩ/ resistive, and capacitive sharing
  Hexagonal pads ø 1 cm
  MgF2 crystal
  CsI photocathode
  150 μm/128 μm drift/ampl. gap

## Slide 24
Multi-Pad Prototype (7-pad)
  200 kΩ,10 MΩ/ resistive, and capacitive sharing
  Hexagonal pads ø 1 cm
  MgF2 crystal
  CsI photocathode
  150 μm/128 μm drift/ampl. gap
Detector R&D for the resistivity value
  Beam
    Muon’s energy (80-150 GeV)
    8 cm diameter of beam
    muons/spill (measured rate ~ kHz/)
Best timing 10MΩ/  : 23.3 0.002 ps
Muons of 150GeV ~ 11p.e/track in DUT
PRELIMINARY

## Slide 25
Uniform Timing Performance
Timing below 30 ps over all area
Diving Into the Details of Our Top-Performing Prototype 10MΩ/
PRELIMINARY

## Slide 26
Signal Sharing
Uniform Timing Performance
  Timing remains below 28 ps during signal-sharing events at the six common corners of the central pad, where signals are usually distributed over three readout pads.
PRELIMINARY

## Slide 27
Spatial Resolution of 1.1 mm
First indications
  Combined tracks in a 20 mm diameter from the central pad.
  Resulted on a spatial resolution of 1.19 mm on X and Y direction

## Slide 28
Particle Beams @ CERN SPS H4
  Electrons 30 GeV
  Calculated rate ~1 MH/cm2
Multi-Pad Prototype (7-pad)
  10 MΩ/ Resistive prototype
  Hexagonal pads ø 1 cm
  MgF2 crystal
  B4C (12min) photocathode
A. Kallitsopoulou : PICOSEC Micromegas Detector, An Innovative solution for Lepton Time Tagging, The 8th International Conference on Micropattern Gaseous Detectors (2024), JINST https://arxiv.org/abs/2501.04991
Facing some ENUBET Requirements

## Slide 29
Particle Beams @ CERN SPS H4
  Electrons 30 GeV
  Calculated rate ~1 MH/cm2
A. Kallitsopoulou : PICOSEC Micromegas Detector, An Innovative solution for Lepton Time Tagging, The 8th International Conference on Micropattern Gaseous Detectors (2024), JINST https://arxiv.org/abs/2501.04991
Facing some ENUBET Requirements
Average 30ps timing resolution on EM showers
Picosec Pad’s
response
Max Amplitude value ~ 175mV

## Slide 30
The 96-pad Detector design
  96 pad prototype
    1cm single cell size
  Custom-made amp. cards in 6 x 16 connector groups compatible for SAMPIC digitizer
  Extended R&D on the PCB design as well as QA/QC
  Preliminary planarity measurements  9um uniformity over full PCB area using stiffener
Advantage:
  Allow the fabrication of large flat boards
Search on Alternative Low Material Budget Approaches
  The ATLAS NSW-like approach
RMS Distance: 9um
X[mm]
Y[mm]
Z[mm]

## Slide 31: The 96-channel prototype single-cell performance
Rise time  1.12ns
PRELIMINARY
Single cell   1cm & 2.5 nm DLC
Best timing: 43.2 0.0052 ps

## Slide 32: Combined response over different pads of the 96-pad prototype
PRELIMINARY
Single cell   1cm & 2.5 nm DLC
Best timing: 43.2 0.0052 ps

## Slide 33: Conclusions
Proof of Concept
  PICOSEC detection concept overcomes timing limitations of gaseous detectors
  Gain can affect robustness and timing resolution
Optimization R&D
  Focus on improving HV stability, preserving signal integrity ( 12.5 0.5 ps )
  Established a consistent way of performing accurate measurements
    Alternative readout geometries ( = 23.5 0.1 ps )
    Photocathode studies ( = 31.9 0.1 ps & = 34.5 0.1 ps )
    Spatial resolution studies ( = 0.5 mm )
    Alternative gas studies ( = 17.1 0.2 ps )
  Large scale developments
    Designed and commissioned successfully different approaches for large scale prototypes up to 20x20 cm2
      ( = 16.8 0.2 ps )
      ( = 23.5 0.4 ps )
    Different solutions for readout electronics and digitization are also mentioned
R&D Toward Applications
  Successful design and commissioning of 96-pad aiming to face the ENUBET requirements
    Detector stability over electromagnetic showers ( = 30.5 0.8 ps )
    Detector stability in high intensity pion beam ( = 60.0 0.1 ps )

## Slide 34: Key Takeaway
Advantage
Deliverable detector up to 20 × 20 cm² with uniform response
and timing below 30 ps
Large pad size  Less electronic channels
Challenge
Ageing of the photocathode material 
Requires Dedicated study

## Slide 35: Thank you
CEA SACLAY
91191 Gif-sur-Yvette Cedex
France
thomas.papaevangelou@cea.fr
alexandra.kallitsopoulou@cea.fr

## Slide 36: In the end, it’s all a matter of timing…

## Slide 37: The Physics of Ionization offers the means for precise spatial measurements (high spatial resolution) but inhibits precise timing measurements
1977
Notes: There were already some very well-established thoughts about timing and the limits we can achieve, due to the physics of ionization. Based on the statistical properties of ion pair production Sauli has stated that there is no hope of improving the time resolution in a gas counter. This was 1977 and several years later Yannis proved him wrong.

## Slide 38
Optimization of geometry and connectivity
Focus on Operational Stability
  Signal Integrity
      Noise reduction
  Parasitic influence
  Capacitance and inductance
Protyping and Testing
  Three boards   10, 13, 15 mm
  Best timing performance with the 10mm metallic prototype 12.5 0.8 ps at the central region
    Thin gap of 125 μm drift gap and CsI photocathode
New Record! 12.5 ps
 10 mm
 13 mm
 15 mm
    More info on Antonija’s Presentation  Design and performance of a new single channel PICOSEC Micromegas detector with metallic and resistive anodes
A. Utrobicic, et al. “Single channel PICOSEC Micromegas detector with improved time resolution, Nuc. Instrum. Meth. A (2024) https://arxiv.org/pdf/2406.05657
Bonus! Reassembly Feature
Notes: The design overview of the single-channel PICOSEC Micromegas detector includes the following key points:
Comprehensive Design Elements: The design encompasses the detector board, the vessel, auxiliary mechanical parts, and electrical connections for high voltage (HV) and signal transmission.
Stability Improvement: The design focuses on enhancing operational stability to better utilize the detector’s capabilities and minimize issues that could arise from external factors.
Noise Reduction: Special emphasis is placed on reducing electronic noise, which is critical for maintaining the integrity of signals and optimizing timing performance.
Signal Integrity: Ensures that the detector’s design maintains signal quality, which is essential for accurate measurements and timing resolutions.
Ease of Reassembly: A streamlined assembly process is implemented, allowing for rapid replacement of detector components, which facilitates efficient testing and measurement with different configurations.
Parasitics Influence: The design takes into account the impact of parasitic capacitance and inductance on output signal integrity, making it a focus area during the design process to mitigate any potential negative effects.

## Slide 39
The μRWELL Approach (JLab)
Based on the same design
  Uses the μRWELL technology for the amplification region
Protypes and Testing
  Different boards with pitch-diameter sizes
    P120-D100, P100-D80, P80-D60
  Best timing performance with the P120-D100 prototype 23.5 0.09 ps at the central region
    Drift gap of 170 μm drift gap and CsI photocathode
 10 mm
A.Pandey. Precise Timing with PICOSEC μRWELL detector-DRD1 Collaboration Meeting https://indico.cern.ch/event/1413681/contributions/5993207/attachments/2879400/5043954/DRD1_talk.pdf
!
50μm
Cherenkov Radiator
photocathode
Notes: The design overview of the single-channel PICOSEC Micromegas detector includes the following key points:
Comprehensive Design Elements: The design encompasses the detector board, the vessel, auxiliary mechanical parts, and electrical connections for high voltage (HV) and signal transmission.
Stability Improvement: The design focuses on enhancing operational stability to better utilize the detector’s capabilities and minimize issues that could arise from external factors.
Noise Reduction: Special emphasis is placed on reducing electronic noise, which is critical for maintaining the integrity of signals and optimizing timing performance.
Signal Integrity: Ensures that the detector’s design maintains signal quality, which is essential for accurate measurements and timing resolutions.
Ease of Reassembly: A streamlined assembly process is implemented, allowing for rapid replacement of detector components, which facilitates efficient testing and measurement with different configurations.
Parasitics Influence: The design takes into account the impact of parasitic capacitance and inductance on output signal integrity, making it a focus area during the design process to mitigate any potential negative effects.

## Slide 40
Increase readout granularity for spatial resolution
Based on the same design
  Uses the  15mm
    Segmented with different pad sizes (3.5mm and 2.2mm pitch)
  To potentially improve the spatial resolution
  Both timing and spatial resolution are mitigated for higher granularity readout (smaller signal amplitudes)
D. Janssens, Robust photocathodes and spatial resolution studies of resistive PICOSEC Micromegas precise-timing detectors- The 8th International Conference on MPGDs https://indico.cern.ch/event/1453371/contributions/6146435/

## Slide 41: A very well understood detector
J.Borteldt, et al. “Modeling the timing characteristics of the PICOSEC Micromegas Detector”, Nuc. Instrum. Meth. A (2021) https://doi.org/10.1016/j.nima.2021.165049
A well understood detector
Simulation Studies using GARFIELD++:
  Modeling Aspects:
  SAT time walk seen in single pe data is explained:
    SAT reduces with avalanche length
    Long avalanches  big e-peak charge
    SAT reduces with e-peak charge
  SAT & Timing resolution are determined by:
    The drift path of the primary photoelectron
             number of photoelectrons in avalanche and its length
Modeling the behavior:
  Phenomenological model describing the dynamical and statistical properties of the detector signal
Agreement between simulation & experimental data
2019
Notes: Physics
  Synchronous Cherenkov photons
  Synchronous Photoelectrons from the photocathode
  Photoelectron conversion(Townset Coeff)
  Preamplification Avalanche
  Transport through the mesh
  Amplification Avalanches

## Slide 42: Detector Testing
Pulsed Laser Beam (IRAMIS/CEA)
  UV Ultra short laser pulses
  Single Photoelectron response
  Perform measurements independently of the photocathode material
  Understanding the properties
Data taking & Output
  Timing reference device – fast photodiode (σΤ ~ 3ps)
  Attenuator meshes to control the number of photoelectrons
  Signal Arrival Time has a dependence on Electron peak charge
  Timing resolution improves with higher drift field & smaller gap(<50ps for 120μm for single pe)
J.Borteldt, et al. “PICOSEC: Charged particle timing at sub-25 picosecond precision with a Micromegas based detector”, Nuc. Instrum. Meth. A (2021)https://doi.org/10.1016/j.nima.2018.04.033
L.Sohl-PhD Thesis “Development of a PICOSEC Micromegas for fast timing in high rate (archives-ouvertes.fr)
2018
Notes: Continuing the collaboration with IRAMIS laser Facility, the way of better understanding of the detector was open. Some detailed studies having the control of number of photoelectrons, resulted to very important statements of detector response.
And say which one are those…
Great achievement of those measurements was that we observed some important statements of the detector response.
The dependence of SAT with electron peak charge in different operation Voltages, The grater the drift voltage the smaller the SAT
In parallel it is evident that timing resolution improves with higher field and smaller gap reaching even a resolution of 50 ps for 120μm gap and

## Slide 43: Simulations
  Modeling Aspects*:
    Phenomenological model describing the dynamical and statistical properties of the detector signal
    SAT time walk seen in single photoelectron data is explained:
      SAT reduces with avalanche length
      Long avalanches  big electron peak charge
    SAT & Timing resolution are determined by:
        The drift path of the primary photoelectron
            number of photoelectrons in avalanche and its length
J.Borteldt, et al. “Modeling the timing characteristics of the PICOSEC Micromegas Detector”, Nuc. Instrum. Meth. A (2021) https://doi.org/10.1016/j.nima.2021.165049
  Mesh Transparency
  Predicting the transparency of Micromegas meshes
  The arrival time on the mesh is sensitive to initial avalanche fluctuations
D. Janssens, Simulating Timing Performance of Micromegas Detector with Garfield++- The 8th International Conference on MPGDs
https://indico.cern.ch/event/1453371/contributions/6146435/

## Slide 44: Scalability…The importance of planarity
The importance of planarity
  1st multichannel prototype tested
  19-hexagonal pad prototype, MgF2, CsI, 200μm drift gap
Variation on timing resolution
  Non uniformity of the drift field gap
  Different gain in single pad area
S. Aune et al, "Timing performance of a multi-pad PICOSEC-Micromegas detector prototype", Nucl. Instrum. Meth.A 993 (2021) 165076,https://doi.org/10.1016/j.nima.2021.165076
2018
All tracks passing within R<2mm from the center of any pad
σ = 25.8 ps
σ = 32.2 ps
19 channel anode 1 cm
*AUTh-Spyros Tzamarias

## Slide 45
Tree possible approaches for modular prototypes with 10x10 active zone :
Rigid, ceramic-core PCB for the MM readout
  Crystal coupled to the PCB with spacers
  MgF2 crystal & MM board will be decoupled from the chamber
  Second PCB will be used for signals towards the amplifiers
Advantage:
  Low material budget on the detector
  Allow the fabrication of large flat boards
The ATLAS NSW Approach
Longer pillars MM module
2021
Ready and operational from CERN-GDD Group
2024+
Ensure the planarity
Notes: Investigating new approaches to build large, robust prototypes

## Slide 46: 100channel PICOSEC Micromegas
100 channel anode  1 cm
“Global” behavior 
excellent homogeneity of the detector
2021&2022
1st prototype tested
  200μm drift gap
  CsI photocathode
  Timing resolution ~25ps
Reducing the drift gap
  180μm drift gap
  CsI photocathode
  Timing resolution ~17ps
    Analysis by Alexandra Kallitsopoulou, Ioannis Maniatis and Spyros Tzamarias. More info in the contribution to the RD51 Collaboration Meeting and “Wide Dynamic Range Operation of MPGDs” workshop, CERN(15-19 November 2021) https://indico.cern.ch/event/1071632/sessions/408832/#20211116
Recovering the resolution in the common corner, for signal-sharing events.
Analytical way of signal Processing
Using Artificial Intelligence- Training a Neural Network
A.Kallitsopoulou-Master Thesis: Development of a Simulation Model and Precise Timing Techniques using Picosec Micromegas Detectors: https://doi.org/10.48550/arXiv.2112.14113

## Slide 47
Signal Processing for Precise Timing
The Standard CDF Technique
  Adjust a curve to the experimental data
    Fitting the leading edge of the waveform with a logistic function
V[V]
T[ns]
Electron peak
Ion tail
  Timing at 20% of peak amplitude for all signals (SAT – Signal Arrival Time)

## Slide 48
Signal Processing for Precise Timing
The Standard CDF Technique
  Finding the total charge of the electron peak
    Fitting additional the falling edge with a normalized logistic function
  Timing at 20% of peak amplitude for all signals (SAT – Signal Arrival Time)
  Create calibration curves
  Subtract the PICOSEC signal from the reference signal

## Slide 49
Signal Processing for Precise Timing
The Standard CDF Technique
  Finding the total charge of the electron peak
    Fitting additional the falling edge with a normalized logistic function
  Timing at 20% of peak amplitude for all signals (SAT – Signal Arrival Time)
  Create calibration curves
  Subtract the PICOSEC signal from the reference signal
  Correct for dynamical errors
  Timing resolution ~
  RMS of the SAT distribution
Muons of 150GeV ~ 11p.e/track in DUT
PRELIMINARY

## Slide 50
Monitoring Plots – Full area detector
Uniformity of response
  Timing Runs with MCP-PMT (trigger) centered on each pad center
Gain Comparison
PICOSEC
MCP-PMT
Pedestal of Detector Baseline noise
Track Mapping over active Area over MCP and PICOSEC alignment

## Slide 51: The role of PICOSEC MM in Muon Monitoring
Sources of muons in ENUBET
  2-body decays of
Muons from
  Emitted at large angles with respect to the beamline
  Can be identified inside the calorimeter
Muons from
  Emitted almost collinear with the beamline
  Can be identified with downstream detectors to the hadron-dump
Embed a PICOSEC-Micromegas layer inside the instrumented hadron damp

## Slide 52: Detector Stability on Pion Beam
Low rate up to 200kHz:
High rate up to 1MHz:
The detector observed to be stable over the full run
80GeV/c pion beam ~ to particles per spill
Beam Size ~2.3 cm x 1.5 cm
B4C 12nm photocathode, achieving timing resolution of 65 ps
Timing resolution degradation due to adjustment of the gain both for the DUT and the reference