## Slide 1
Radius disco
Motor Controller
Sensor
Motor
soporte
Radius agujero

## Slide 2
Radius disco
Motor Controller
Sensor
Motor
soporte
Radius agujero
servo

## Slide 3
Overall Conceptual Design
Air
X2
Cryostat
Black Box
2 feedthroughs CF40, each with 3 optical feedthroughs
6 SMA optical fibers from feedthrough to black box
black box containing light source
black box on top of cryostat

## Slide 4: Black box concept
Power supply
Test pulser
Control
Reference sensor/
Distribution board
LED coupling to optical fiber
Test pulser
Test pulser
Test pulser
Test pulser
Test pulser board 5
Voltage: 0~20V
Trigger 0
Trigger 1
Trigger 2
Trigger 3
Trigger 4
Trigger 5
pulsed light
reflected light
Integrated light signal
Ehernet comunication
Trigger 0..5
light to SMA0
light to SMA1
light to SMA2
light to SMA3
light to SMA4
light to SMA5
Outside black box
Bias voltage led pulsed
Bias voltage reference sensor

## Slide 5: Control board
Beagle bone black
  Embedded linux inside
  7 Channels ADC
    Reference ouput sensor
    Temperature
  Comunication with Power supply
    Python library
  PWM to trigger pulsed LED boards
  Control integration window.
    Timing has to be improved
    Developing code for real time units inside beaglebone
  To be develop the user control software.
    Web server interface through wireless (general network)
    OPC-UA server though tehcnical network (evaluating)

## Slide 6: Reference sensor/ distribution board
Reference sensor
  SensL SiPM (up left)
    Fast output (down)
    Slow output (to be used)
  Integrator (up right)
    Limited sampling rate in control board (200kS)
    Developing control for integrator window.
    Analog output to control board
  Developing test to adquire the full channel (sensor + integrator + ADC)
Distribution board
  Distribute Bias voltage
    Common to all LED pulser boards
  Distribute trigger
    From the control board to each connector to LED pulsed board.
  TTL trigger for the charge readout
  Control comunication through TTL signals
    6 trigger, 2 for integrator, 2 analog signals
Both functionlities will be implemented in one board
To be designed as soon as finished the test with the full chanel

## Slide 7: LED coupling cavity
Black box
Kaputschinsky with blue LED
Optical fiber
PMT/SiPM
Based on Thorsten idea
3D printed
Tested in all 6 positions and measured power entering fiber with powermeter
Large variations from position to position: ~2 factor
Tested same position several times: roughly the same
=> Sensitive to placing of Kaputschinsky PCB but might be better with final PCBs and long LEDs (by mistake legs of these was cut)

## Slide 8: LED pulsed light board result
All measurements has been done with a powermeter bought for the test
Overlayed measurements for diferent frequencies (100 .. 10kHz)
Power normalized to 1kHz
It doesn’t depend of pulse frequency
There are not time dependency
at 1 kHz up to 1.8 nW
Power vs voltage
Power vs time (h)
7 V
8 V
19.5 V

## Slide 9: Powermeter vs SiPM Output
Chart: Powermeter vs SiPM Output
| 0 | 0 | 0 | 0 | 0 | 9.1743119266055034E-3 | 2.7522935779816557E-2 | 5.5045871559633031E-2 | 0.10550458715596328 | 0.18348623853211052 | 0.26605504587155965 | 0.37614678899082626 | 0.50458715596330195 | 0.65596330275229353 | 0.81651376146788957 | 1 | 1.1834862385321099 | 1.36697247706422 | 1.5229357798165148 | 1.5871559633027541
Fast SiPM Output (Positive Integral) | 0 | 0.0010184 | 0.011566 | 0.011784 | 0.019422 | 0.021023 | 0.024733 | 0.069761 | 0.040009 | 0.12737 | 0.22514 | 0.35331 | 0.50171 | 0.64683 | 0.82578 | 1 | 1.1804 | 1.351 | 1.5565 | 1.6223
Slow SiPM Output | -0.0002588 | -0.00016756 | 0.00080777 | 0.0011809 | 0.0025852 | 0.006412 | 0.025951 | 0.061484 | 0.11859 | 0.19873 | 0.28664 | 0.407 | 0.53823 | 0.68876 | 0.84099 | 1 | 1.1562 | 1.2954 | 1.4057 | 1.4643
Linear | 0 | 0 | 0 | 0 | 0 | 0.0091743 | 0.027523 | 0.055046 | 0.1055 | 0.18349 | 0.26606 | 0.37615 | 0.50459 | 0.65596 | 0.81651 | 1 | 1.1835 | 1.367 | 1.5229 | 1.5872
SiPM ouput is measured with an oscilloscope
Powermeter is at the end of optical fiber after LED coupling
Positive integral by computing
Slow output is no lineal at high power

## Slide 10
Results from CIEMAT:

## Slide 11
Results from CIEMAT:
If true, calibration will take long => All PMTs should be calibrated simultaneously
Although still not sure how this should work in a LAr TPC with Ar-39 + Saturation sets in a very small Nphe values

## Slide 12: Status and Plans
Pulsing all 6 LEDs at the same time makes idea of reference sensor useless in principle
Options:
  Measure power for each LED first and then switch on all LEDs at the same time
  Use only one of the LEDs and a 1-7 splitter as in the cryostat => 1 LED to rule them all
Will continue to develop the system for 6 LEDs