## Slide 1: Gas Detector R&D at IFAE
Thorsten Lux

## Slide 2: Gas Detector Principle
Charged particles
X-ray
(UV) Photons
Cathode
Anode
Amplification
Provides:
xy position
Energy
(z position)
e-
CsI coating
Gas (Mixture)
mm - m
E (+ B)

## Slide 3: Charge Transport in Gas
ELECTRIC FIELD E = 0: THERMAL DIFFUSION
ELECTRIC FIELD E > 0: DRIFT AND DIFFUSION
E
IONS
ELECTRONS

## Slide 4: Drift
Electrons:
Drift velocity complex function of E field
normally in the order of few cm/s
Ions:
Drift velocity  E field
very slow, several 1000 times slower
 causes sometimes problems

## Slide 5: Diffusion
Drift
Electrons:
point-like charge cloud gets wider with drift distance
 = D*sqrt(z)
transversal (E) and longitudinal diffusion (E||)
transversal affects point resolution
longitudinal affects time information
B||E can reduce transversal dramatically
Ions:
Diffusion much smaller but rarely used in real detectors
=> Remember Federico’s graphene talk!
Drift
E Field
sT
sL
time

## Slide 6: Diffusion
TRANSVERSE DIFFUSION:
LONGITUDINAL DIFFUSION:

## Slide 7: Charge Amplification
Recombination Region
Ionization Region
Proportional Region
Limited Proportional
Region
Geiger-Mueller Region
Continuous Discharge Region
Pulse Height
high voltage




## Slide 8: Maximal Gas Amplification
in Argon

## Slide 9: Gas Choice
Right gas choice fundamental for optimal operation! Depends strongly on application.
Normally noble gas + some additive gases
Important factors:
stopping power
energy resolution
costs: direct (e.g. Ar cheaper than Xe) and indirect ( e.g. pressure vessel)
…
We can also play with the pressure
pressure 

## Slide 10: Quencher Gases
Pure noble gases are often not suitable:
slow
relatively large diffusion
stable amplification limited
 Solution: Adding some amount of molecular gas
Some examples:
But … this can also complicate things:
more sensitive to impurities -> attachment, loss of electrons during drift
gas system might become more complex -> purification, flammability

## Slide 11: Gas Amplification Technologies
Wire readout (classically used)
Gas Electron Multiplier (GEM)
Micromegas
Wire Readout the classical technology
E x B effects
ions might drift back to gas volume
wire under tension requires a lot of material
slow ion signal
good reasons to look for alternatives:
Charge amplification, for light amplification see Alfonso’s talk (soon)

## Slide 12: Micro Pattern Gas Detectors
Several advantages about the classical wire readout:
Excellent spatial resolution ( amplification structures: ~100 m)
Very good energy resolution
Low material budget
No ExB effects
Cheap
Can be produced in large quantities
GEM

## Slide 13: MicroMegas (MM)
1 stage amplification
Excellent energy resolution and low threshold (600 eV)
Time resolutions below 1 ns possible

## Slide 14: Gas Electron Multiplier (GEM)
Amplification within holes of Kapton foil coated with copper
Normally operated in cascades -> better stability
Can be operated in high rate environments (LHCb: 1 MHz/cm2)

## Slide 15: Real Detector: ALICE TPC
~ 5 m
88 m3

## Slide 16: Tracking with a TPC

## Slide 17: Particle Identification
Measuring dE/dx and momentum (if B is present) allows PID!

## Slide 18: IFAE Gas Detector Projects
T2K TPCs -> see also talks from Javi (last month) and Stefania (soon)
EL TPC -> see R&D talk of Alfonso (soon)
LAr double phase prototype
Si-MPGD with MediPix readout
(8.2 ± 0.1)% FWHM
xenon
18

## Slide 19: T2K: MPGD Detector R&D
2005: Start R&D efforts for a MPGD TPC for T2K
European GEM collaboration: UniGe, IFIC, INFN Bari, IFAE
19/19
2 GEM tower
3 GEM each
~20x24 cm2
also small setup at IFAE

## Slide 20: T2K: MPGD Detector R&D

## Slide 21: T2K: MPGD Detector R&D
IFAE participated in setting up testbench
characterization of ~ 90 MM modules
~12 m2 readout area
nowadays focus on analysis

## Slide 22: DLAr 6x6x6 m3 Prototype
Currently in the decision phase (CERN and Ministry)

## Slide 23: DLAr 6x6x6 m3 Prototype
Contributing to the primary scintillation light detection (together with CIEMAT)
Tests with microbulk MM in Ar:iC4H10 and pure argon -> final project of Raul

## Slide 24: Si-MPGD Project (CNM/IFAE)
To exploit the full imaging capabilities of MPGDs classical pads are too large
Solution: Couple MPGD to MediPix/TimePix
Aiming on improved sensor fully Si
55x55 m2 pixel size
256x256 pixel
14x14 mm2 active area
2 relevant modes:
  Time over Threshold
  Time of Arrival
already used in previous CNM/IFAE project: DearMama

## Slide 25: Summary
Gas detectors are a very flexible detector type
Suitable for charged particles, X-rays and photons
Choice of gas mixture and operational pressure allows optimization
MPGD technologies gave new push
TPCs allow 3D reconstruction of event + PID
I had to skip many details as e.g. attachment, …
IFAE built up during the last 9 years some experience with gas detectors
More talks about the specific projects

## Slide 26: Drift Velocity

## Slide 27: How it looks like
MM
GEM