## Slide 2: Overview of Beam Dump Facility and SHiP experiment at CERN
M. Casolino on behalf of BDF working group and SHiP Collaboration
IFAE, 16th November 2018
Acknowledgements: C. Ahdida, M. Calviani, R. Jacobsson, K. Kershaw, M. Lamont, E. Lopez Sola, N. Serra, H. Vincke

## Slide 3: Outline
Motivation
BDF concept and requirements
  Details about the target and the target station
  RP challenges
SHiP
  Detectors
  Physics performances
Summary
IFAE, 16th November 2018

## Slide 4
A successful theory…
The Standard Model (SM) describes the interactions between all known elementary particles, accounting for three of the fundamental forces of Nature.
IFAE, 16th November 2018

## Slide 5
..but BSM is behind the corner
Not a complete unified theory, what about gravity?
Why three generations?
No mass term for neutrinos
Not enough CP-violation to explain matter-antimatter asymmetry
No candidate for Dark Matter
Naturalness and Hierarchy problem
Chart: 
| NORMAL MATTER | DARK MATTER | DARK ENERGY
 | 5 | 25 | 70
IFAE, 16th November 2018

## Slide 6
We live in a Dark Universe
It is roughly 80% of the matter in the universe
Interact with other particles weakly
It has mass, so gravitational effects  only method with evidence until now
WIMP miracle  mNP~ΛEW
Chart: 
| NORMAL MATTER | DARK MATTER | DARK ENERGY
 | 5 | 25 | 70
IFAE, 16th November 2018

## Slide 7
A voyage into the unknown
GeV
WIMPs
LDM
IFAE, 16th November 2018

## Slide 8
WIMP searches – Direct production at LHC
detection method
No evidence yet
Still looking
TeV
TeV
IFAE, 16th November 2018

## Slide 9
WIMP searches – Recoil method
Dark matter in the halo of our galaxy
On the earth we can detect a wind of Dark Matter
IFAE, 16th November 2018

## Slide 10
WIMP searches – Recoil method
No evidence here as well
IFAE, 16th November 2018

## Slide 11
Portals to Hidden Sectors
WIMP absence  Hidden Sectors idea
Dark Matter naturally light (LDM) (mNP<10 GeV)
Low Production branching ratios (<10-10)
Long-lived objects
IFAE, 16th November 2018

## Slide 12
Many Portals
SM can be connected to the hidden sector (HS) through different mediators:
Scalar (e.g. dark scalar, dark Higgs)
Vector (e.g. dark photon)
Fermion (e.g. heavy neutral lepton (HNL))
Axion-like particle (ALP)
To minimize model dependence full reconstruction and PID are essential
Main experimental challenge is background suppression
IFAE, 16th November 2018

## Slide 13
Example: Fermionic Portal
Still 3 missing pieces to the SM that can solve many experimental problems:
Adding 3 RH Majorana neutrinos Ni:
  Light N1 with mass ~keV  dark matter candidate
  Heavy N2,3 with mass ~GeV and weakly coupled to SM
    Create baryon asymmetry of the universe via leptogenesis
    Produced in charm decays; detectable via visible decays
Best sensitivity to HNLs  Beam Dump Facility with heavy target
IFAE, 16th November 2018

## Slide 14
Experimental concept
High Intensity beam into an heavy target (12λint):
  Maximize NP particles production
  Particles either coming from heavy meson decays or from pN interactions
  Suppress pion and kaon decays which is source of background
Minimize the flux of SM particles in the detector
Define a (large) fiducial volume where the background level is approximately zero
Detection by decay or by interaction with matter (recoil method)
IFAE, 16th November 2018

## Slide 15
CERN accelerator complex
Exploit full power of the SPS:
  About 20% running for LHC physics
  80% available for fixed target experiments!
Antimatter factory
High energy experiments and test beams
Low energy experiments and test beams
Former CNGS line
IFAE, 16th November 2018

## Slide 16
SPS North Area
Slow extracted beam at 400 GeV/c
New beam line to be added to the already existing ones
The reduction of the extraction losses is the most complex challenge
BDF target
To build
IFAE, 16th November 2018

## Slide 17
SHiP overview
BDF target and target complex
IFAE, 16th November 2018

## Slide 18
BDF is a proposed permanent facility in the North Area at CERN
High intensity proton beam slow extraction: 4*1013 p+/pulse, 355 kW average beam power, 2*1020 pot/5 years → Design of the facility driven by RP constraints due to prompt/residual dose
Location close to experimental and public areas → Minimize impact on other facilities and environment
Dense TZM and W target → High activation expected
Keep flexibility for future installations
CE layout of BDF and surrounding facilities
BDF at SPS
IFAE, 16th November 2018

## Slide 19: BDF target - Operational conditions
Dilution of the beam by the upstream magnets
  Beam dilution optimization:
    Target mechanical performance
    Magnets aperture limits
  50 mm radius, 4 turns in 1 second
Large beam spot: 8 mm 1σ
Baseline characteristics | 
Proton momentum | 400 GeV/c
Beam intensity | 4.0·1013 p+/cycle
Cycle length | 7.2 s
Spill duration (slow extraction) | 1.0 s
Average beam power deposited on target | 320 kW
Average beam power on target during spill | 2.6 MW
4·1013 ppp
7.2 s
1 s
Challenging target design
IFAE, 16th November 2018

## Slide 20: BDF target - Design
Main functions:
  Full SPS 400 GeV/c beam absorption  Target/dump
  Maximize the production of charmed mesons  physics performance
Material requirements:
250 mm diameter cylinders
Total length ~ 1.5 m
Optimized segmentation of the target to minimize the level of temperatures and stresses
High power deposition
forced water cooling required
5 mm gap between the blocks
~1.5 m
Ø250 mm
  1st part: TZM core
  Molybdenum alloy, higher strength and recrystallization temperature than pure Mo
  2nd part: Tungsten core
  High-Z and good performance under irradiation
  Ta/Ta2.5W cladding
Ta cladding to avoid corrosion/erosion effects
Achieved via Hot Isostatic Pressing (HIPing)
  High-Z materials
  Short interaction length
Increase the reabsorption of pions and kaons
IFAE, 16th November 2018

## Slide 21: BDF target - Cooling
Inlet
Outlet
Water flows through 5 mm gap between the target blocks
  Cooling of circular face of the blocks critical
   beam impact
Homogenous water speed in the channels ~ 5 m/s
Average Heat Transfer Coefficient ~ 20000 W/m2K
Minimized mass flow rate: 10 kg/s
Pressure supply: 20 bar
    Increase water boiling temperature above 200°C
    Avoid vapor formation in contact with target block
  2 parallel streams in series
   avoid cooling failure in case of blockage of one channel
Preliminary design of the target cooling circuit
Total Δp ~ 3 bar
IFAE, 16th November 2018

## Slide 22: BDF target - Thermo-mechanical calculations
High raise of temperature during beam impact: temperature limitations in the Ta cladding  vapor formation, plastic deformation of the cladding
The high temperatures reached lead to a high level of stresses
Properties of pure Ta at high temperatures not compliant with stresses chosen cladding material: tantalum-tungsten alloy, Ta2.5W
Max temperature
Ta cladding 180°C
Chart: Temperature evolution after beam impact
ΔTTantalum ~ 140°C per pulse!
Maximum Von Mises equivalent stress ~110 MPa
IFAE, 16th November 2018

## Slide 23
Target is located 15 meters underground
Iron hadron absorber encloses production target
Target and hadron absorber are inside a He vessel
  To avoid corrosion and air activation
Fully remote handling/manipulation
Significant attention to radiation protection
Crane and trolley concepts → equivalent shielding, but target handling safer with trolley
BDF target complex
Crane concept overview
Trolley concept overview
Target and hadron absorber
Facilitates target exchange → safer interventions
Submitted to JINST (arxiv:1806.05920)
IFAE, 16th November 2018

## Slide 24
Crane concept – target exchange
IFAE, 16th November 2018

## Slide 25
Trolley concept – the trolley
IFAE, 16th November 2018

## Slide 26
Trolley concept – target exchange
IFAE, 16th November 2018

## Slide 27: RP considerations for the BDF target complex
High prompt dose in BDF target area calls for adequate shielding around the target
Only absolute necessary equipment should be installed in “hot” areas
Depending on residual dose rate and tasks, manual interventions should partially/completely be replaced by remote maintenance/repair
Air volumes to be minimized in ‘hot’ areas or to be replaced by He/vacuum environment
Static confinement of air by physical barriers to separate air in contaminated areas from outside
Dynamic confinement by a ventilation system guaranteeing a pressure cascade from low to high contaminated areas
Water cooling circuits for highly radioactive elements should be closed and separated from others
Activation and contamination of ground water and earth to be avoided
The design must consider minimization, decommissioning and dismantling of radioactive waste
Water and Ground activation
Radioactive waste
Air and He activation
Prompt and residual radiation
Radiation Protection
IFAE, 16th November 2018

## Slide 28
BDF/SHiP as implemented in FLUKA
No access during operation into the detector hall is the main condition for current design
Massive shielding to keep prompt/residual dose rate and airborne radioactivity as low as possible
Most critical area was embedded in He-environment
Shielding was optimized to reduce ground activation to negligible levels
Active muon shield with magnets (1.8 T) from the SHiP experiment was included
Concrete
Helium Vessel
Target
Magnetic part of hadron stopper
Active muon shield magnets
11 m
4.5 m
Target hall
Detector hall
Moraine
Cast Iron
y
z
x
29 m
RP evaluation based on FLUKA simulations
Side view
Cross-sectional view
Moraine
Concrete
Target Hall
Cast Iron
Helium Vessel
0.8 m
0.6 m
2.0 m
1.5 m
3.2 m
0.5 m
1.5 m
Target
y
x
z
IFAE, 16th November 2018

## Slide 29
Target area:
Prompt dose rates reach ~100 mSv/h above He-vessel and drop down to < 1 µSv/h above top concrete shielding (conservative gaps)
→ Expected classification: Supervised Radiation Area (up to 2000h/year) (< 3 µSv/h) in the target hall
Residual dose rates of a few µSv/h above and next to He-vessel
Very high residual dose rates next to target and cast iron shielding O(100) Sv/h
→ Remote handling and designated storage areas are therefore foreseen for these elements
100 rem = 1Sv
Expected dose rates in the target and experimental area
Prompt dose rate at 4×1013 p / 7.2s
Residual dose rate at 2×1020 pot (1 week cooling)
Experimental area:
Prompt dose rates reach ~100 mSv/h at magnet mainly due to muons
Residual dose rates close to first part of muon shield reach ~10 µSv/h
→ Expected classification during beam off: Supervised Radiation Area (<15 µSv/h) or Simple Controlled Radiation Area (<50 µSv/h) in experimental hall
IFAE, 16th November 2018

## Slide 30
SHiP overview
IFAE, 16th November 2018

## Slide 31
Active muon shield
Distribute the bkg over a long spill: 4x1013 p/ 7.2s
Sweeping magnet
Decay volume to be far away from the walls
Heavy target stops hadrons before the decay. After the target and the hadron absorber only muons survive
Muons come mainly from η, η’, ω
IFAE, 16th November 2018

## Slide 32
Active muon shield
Optimization of the magnetic field with Machine Learning techniques
Challeging aspects:
Narrow separation between field directions
Aiming to 1.7T to minimize lenght ( with grain oriented steel sheets)
Have reliable muon sample to optimise
The muon shield is the critical component to optimise to maximise the experimental acceptance
Reduces the background by 6 orders of magnitude (in the fiducial volume background free experiment)
Kinematic range up to p~ 350 GeV and pT ~ 8 GeV
IFAE, 16th November 2018

## Slide 33
SHiP overview – Emulsion detector
High spacial resolution to observe the τ decay (~1mm flight length)
Electronic detector for tracking to give the time stamp of the event
Target to measure the τ products
Muon magnetic spectrometer for muon identification
IFAE, 16th November 2018

## Slide 34
νtau- Physics
IFAE, 16th November 2018

## Slide 35
iSHiP
DM particles can scatter on the electrons or nuclei of the dense material of the Emulsion Spectrometer in the Upstream Detector
Difficult to beat the sensitivity of Missing Mass Experiments for vWINPs coming from Dark Photon, but for other models (e.g. scalar, Z’) SHiP might have a unique sensitivity
IFAE, 16th November 2018

## Slide 36
Accelerator based LDM searches
Emulsion detector ideally suited for Light DM
searches thanks to:
1) micrometric position resolution
2) mrad angular resolution
3) High electron identification efficiency
χ could be lighter than HS mediator (e.g. V) V→ χ χ allowed
With 1020photons in SHiP:
A LDM beam downstream the dump
Scattering experiment χe→ χe on the atoms of the SHiP detector (emulsions)
LDM search beyond relic density
IFAE, 16th November 2018

## Slide 37
Fiducial Volume
To have a background free experiment need of a fiducial volume with at least 10-3 mbar to have negligible background from neutrinos interacting in the air
Veto system around the fiducial volume:
Liquid or plastic scintillating in the vacuum vessel walls for vetoing
Upstream veto before the entrance window
Tracking veto after ~5m of the entrance window
IFAE, 16th November 2018

## Slide 38
HS Spectrometer
1) Fully reconstructed signal: at least two charged particles e.g. Nμ+π- or Nρ+μ-
2) Partially reconstructed signal (neutrinos in the final state) e.g. Nμ+vv
3) Fully neutral channels e.g. A—> γγ
IFAE, 16th November 2018

## Slide 39
Backgrounds
IFAE, 16th November 2018

## Slide 40
Physics Performance – Dark Photon
Production at SHiP:
Meson decays e.g. π0 → γV (~ε2)
p breamsstrahlung on target nuclei pp → ppV
Large mV  direct QCD production through underlying
arXiv:0906.5614
arXiv:1311.3870
arXiv:1205.3499
Decay:
IFAE, 16th November 2018

## Slide 41
Physics Performance – Dark Scalar
IFAE, 16th November 2018

## Slide 42
Physics Performance – ALPs
Pseudo-scalar can arise from spontaneously broken U(1) symmetry:
An example is the axion, introduce to solve the strong CP problem (m ~10-5 eV)
Axion-Like particles (ALPs) can arise from other broken symmetries
ALPs can couple to: gauge bosons, fermions or gluons
Coupling proportional to 1/fa (scale of the spontaneous broken symmetry)
IFAE, 16th November 2018

## Slide 43
Physics Performance – HNL
Production and decays are both suppressed by U2 , so the sensitivity is proportional to U4
If the mass is small enough they can be produced in semileptonic meson decays (pions, kaons, D-mesons, B-mesons), at higher masses they will be produced by W and Z
IFAE, 16th November 2018

## Slide 44
Physics Performance – HNL
IFAE, 16th November 2018

## Slide 45
Summary and conclusions
SHiP intends to explore the intensity frontier searching for long-lived and very weakly interacting particles:
Possibility to search a broad variety of signals
• SHiP also hosts a compact neutrino detector to perform SM physics studies
  it can be used to search indirectly for HS particles via the vWIMP scattering
HS particle can be searched for in an inclusive way in the fiducial volume
Many challenges have been faced for the target complex and the detectors
Roadmap for Dark Matter discovery:
Decision on approval following conclusion of the ESPP (end 2019):
Construction: 2021-2026
Start of data taking after Long Shutdown 3
IFAE, 16th November 2018

## Slide 46
Thank you for your attention!

## Slide 47
PBC
IFAE, 16th November 2018

## Slide 48
SHiP detectors
IFAE, 16th November 2018

## Slide 49
SHiP detectors
IFAE, 16th November 2018

## Slide 50
SHiP detectors
IFAE, 16th November 2018

## Slide 51
Background estimation
IFAE, 16th November 2018

## Slide 52
IFAE, 16th November 2018

## Slide 53
IFAE, 16th November 2018

## Slide 54
IFAE, 16th November 2018

## Slide 55
IFAE, 16th November 2018

## Slide 56
IFAE, 16th November 2018

## Slide 57
IFAE, 16th November 2018
Light ALPs

## Slide 58
IFAE, 16th November 2018

## Slide 59: Target assembly design
Target inner tank
  Supports target core blocks
  Encloses the target cooling system
Target outer tank
  Water-leak tightness
  Provides interfaces with water and electrical connectors
  Dry environment + leak monitoring
  Replacement of the whole box in case of target failure
  Compatible with target complex handling and integration design
Target outer tank
Target tank enclosed inside a Helium containing box
IFAE, 16th November 2018

## Slide 60: Material R&D – Use of Ta2.5W
Target cladding material: Ta2.5W
  Bonding quality with tungsten and TZM expected to be the same
Cladding material | Maximum Von Mises eq. stress expected | Yield strength | Safety factor
Tantalum (preliminary design) | 110 MPa | 80 MPa (at 180°C) | 0.7 ✗
Ta2.5W (new design) | 110 MPa | 200 MPa (at 180°C) | 1.8 ✓
Chart: Ta and Ta2.5W strength comparison
| 25 | 100 | 150 | 200 | 250
Ta Yield strength | 185 | 125 | 90 | 70 | 65
Ta Tensile strength | 200 | 190 | 190 | 185
Ta2.5W Yield strength | 250 | 210 | 189 | 176
Ta2.5W Tensile strength | 344 | 331 | 290 | 276
  Good corrosion-erosion resistance
  Higher strength, specially at high temperatures
  2.5% content of W
  Similar thermal properties to Ta
Additional considerations:
Fatigue properties for 107 cycles
Radiation damage (ongoing)
IFAE, 16th November 2018